## Slide 1: Longitudinal stability of 12 bunches s 31st of July 2018
J. Repond, E. Shaposhnikova
Acknowledgements: G. Papotti, T. Bohl, H. Bartosik, SPS OP crew
LIU-SPS Beam Dynamics Working Group

## Slide 2: MD 12 high intensity bunches, double RF operation Study of effects of the voltage ratio on beam stability
LHC nominal momentum and RF cycles
12 bunches with nominal longitudinal emittance (0.35 eVs)
LLRF activated: Feedback, Feedforward, Longitudinal Damper, Phase and Synchro-loops (no controlled emittance blow-up)
Injected bunch intensities between ppb and ppb
Double RF operation with a constant ratio during cycle,
The ramp starts at 11.1 s and finishes at 19.53 s

## Slide 3: Stability threshold during ramp, 12 bunches Energy dependence in a single RF system
Instabilities at flat bottom were observed not reproduced in simulation
What is the effect of the 800 MHz RF system?
Presented last year

## Slide 4: Intensity treshold during ramp, feedback off 12 bunches SRF: simulations vs measurements
Intensity threshold with feedback off, single RF system
Matched bunches in simulations
End of ramp and flat top well reproduced in simulations with correct bunch length
Difficulties to reproduce flat bottom instability
  Short flat bottom in simulation (1s)
  Bunch rotation in PS before extraction (s-shape)
  Missing impedance?
Presented last year

## Slide 5: Stability treshold during ramp 12 bunches: simulations vs measurements
Steady-state formula of impedance reduction from feedback gives reasonable agreement
   Increasing bunch length with intensity removes the energy dependence
Presented last year

## Slide 6: Stability threshold at flat top Comparison between ramp simulations and measurements
Bunch distribution in simulation is matched at flat top
   Bunch distribution after ramp can differ from matched at flat top
Measured threshold at flat top is compared with simulations
 Measurements of stable beams and simulations (FT and ramp) are in good agreement with feedback off
7 MV, single 200 MHz RF system, 12 bunches, feedback off
Stable beam
Measurements of unstable beam during ramp cannot be compared here
no information about bunch length at flat top
Presented last year

## Slide 7: Instability at flat bottom
Bunch length [ns]
12 unstable bunches at flat bottom, single RF, ppb
Injected bunch length 3.3 ns
Bunch length after filamentation: 2.7 ns
Instability at flat bottom after 4 s
Presented last year
Instability observed but not reproduced yet in simulation
  Problem of accuracy in the induced voltage calculation
  Bunch distribution, long flat bottom
  LLRF (phase-loop)
  Missing impedance?
Can the 800 MHz RF system cure the instability at flat bottom?

## Slide 8: Beam stability with 12 highest intensity bunches as a function of the voltage ratio between the two RF systems
Bunch length evolution,
Bunch length evolution
High intensity beams unstable at flat top with low voltage ratio ()
Can be stabilized by increasing the voltage ratio
   Bunch length oscillations with larger amplitude at flat bottom for a larger voltage ratio (similar observations with lower intensities)
Intensity at injection: ppb, decreases to ppb during the flat bottom,
nominal 200 MHz voltage program ( MV at injection, MV at flat top),

## Slide 9
Beam stability with 12 lower intensity bunches as a function of the voltage ratio between the two RF systems
Bunch intensity injected
ppb
 Improved stability at flat top with large ratio but larger oscillations at flat bottom observed
Bunch intensity injected
ppb

## Slide 10
Beam stability with 12 lower intensity bunches as a function of the voltage ratio between the two RF systems
Bunch intensity injected
ppb
Bunch intensity injected
ppb
 Same observations with lower intensities: improved flat top stability with a larger voltage ratio but larger oscillations at flat bottom

## Slide 11: Bunch length (FB) versus bunch intensity for different voltage ratios
A small voltage ratio improves the stability at flat bottom (compared to r=0)
Larger oscillations with increasing ratio, why?
Data from last year
Batch of 12 bunches, nominal LHC voltage program. Bad beam quality last year compared to 2018.
The error bars represent the maximum amplitude of the bunch length oscillations
Different scales!
FB on, FF on

## Slide 12: Bunch profile evolution during cycle, large tails at FB with a large voltage ratio (0.25)
Bunch line density measured during cycle
Synchrotron frequency at FB
for different voltage ratios (BSM)
For voltage ratios > 0.1
the bunch has a flat portion in the synchrotron frequency distribution

## Slide 13: Synchrotron frequency distribution during cycle for different voltage ratios with (BSM)
The plateau in the synchrotron frequency distribution at flat bottom (r > 0.1) gives a large coherent response explaining the oscillations observed
Large spread at flat top for every ratio  Improved stability
Impossible to increase the synchrotron frequency spread at flat bottom?
− Flat top
− Flat bottom

## Slide 14: Synchrotron frequency distribution, Effect of phase shift between the two RF systems
A negative phase shift from the bunch-shortening mode reduces the plateau in the synchrotron frequency distribution
The same behaviour observed for other voltage ratios
/!\ The acceptance is reduced with a phase shift (to be checked!)
Synchrotron frequency distribution
, different
Derivative of the synchrotron frequency
, different

## Slide 15: Maximum emittance during cycle for different voltage ratios with (BSM)
Taking into account controlled emittance blow-up the voltage ratio can be increased to 0.15 after ~16 s and to >0.2 after ~18 s
Maximum emittance is the critical one if crosses zero or the acceptance if no plateau
Momentum cycle (LHC nominal)
eVs
eVs
Critical emittance is defined by the emittance of the first zero crossing of or the one closest to zero
Voltage ratio during cycle, first approximation

## Slide 16: Critical emittance at flat bottom Effect of phase shift between both RF systems
A negative phase shift from the bunch-shortening mode increases the bunch emittance without flat portion in the synchrotron frequency distribution
The stability is not necessarily ensured but lower coherent response expected
The acceptance is reduced with a phase shift (to be checked!)
* Critical emittance is defined by the emittance of the first zero crossing of or the one closest to zero
*
*
*
Derivative of the synchrotron frequency
, different
Critical emittance as a function of
for different (shaded area = no zero crossing)

## Slide 17: Synchrotron frequency distribution and intensity effects An example from simulations at flat bottom, 2 RF,
Frequency shift from intensity effects  changes the plateau
Due to beam loading, each bunch sees a different synchrotron frequency shift and a different phase of the 800 MHz
To be checked in simulations!
Beam of 12 bunches, 3 ns long with ppb
Synchrotron frequency distribution
with and without intensity effects (bunch 1 and 12)
Distribution of particles in synchrotron frequency,
bunch 1 and 12
Single RF: peak at ~4%, ~650 Hz

## Slide 18: Bunch length (FT) versus bunch intensity for different voltage ratios
Improved stability at flat top with increasing voltage ratio
Data from last year

## Slide 19: Conclusion
The high intensity beam with 12 bunches ( ppb injected) can be stabilized by increasing the voltage ratio
For voltage ratios at flat bottom, large bunch oscillations are observed
  This is the effect of the flat portion in the synchrotron frequency distribution which induces a large coherent response.
To increase further the synchrotron frequency spread at flat bottom the phase difference between both RF systems can be adjusted
  A negative frequency shift from the bunch-shortening mode can remove the plateau
At flat top the voltage ratio can be increased to 0.25 (maximum before creation of smaller buckets) to increase the synchrotron frequency spread

## Slide 20
THANK YOU FOR YOUR ATTENTION!

## Slide 21: Synchrotron frequency distribution and intensity effects An example from simulations at flat bottom, 1RF vs 2 RF (10%)
1RF
2RF

## Slide 22: Bunch length comparison with different voltage ratio (>0)
Flat bottom
Flat top

## Slide 23: Bunch length comparison with different voltage ratio
Flat bottom
Flat top

## Slide 24
ppb
ppb
ppb
ppb
ppb

## Slide 25
ppb
ppb
ppb
ppb
ppb

## Slide 26
ppb
ppb
ppb
ppb
ppb

## Slide 27
ppb
ppb
ppb
ppb
ppb

## Slide 28
ppb
ppb
ppb
ppb