## Slide 1: Slip–stacking simulations with intensity effects
D. Quartullo
Acknowledgements: T. Argyropoulos, A. Lasheen,
E. Shaposhnikova, the BLonD team

## Slide 2: Contents
Introduction
Slip-stacking fundamentals
Slip-stacking in SPS
Results for Q20 optics
  Parameter optimizations
  Suggested solution
Results for Q22 and Q26 optics
Conclusions and next steps

## Slide 3: Introduction (1/2)
HL-LHC requirement: to double peak luminosity after LS2
    Increase the number of bunches in the LHC
LIU baseline to achieve that is to decrease bunch spacing from 100 ns to 50 ns in SPS through slip-stacking
    Basic idea: let two batches move in longitudinal phase space and interleave -> bunch spacing divided by two!
Slip-stacking used at Fermilab to double beam intensity

## Slide 4: Introduction (2/2)
Potential slip-stacking feasibility is based on large bandwidth of the 200 MHz RF system
Slip-stacking can be tested only after LS2
  LLRF of 200 MHz RF system has to be upgraded
Simulations are the only means to check slip-stacking feasibility
  In case of bad outcome alternative scenarios have to be found [1]
Some preliminary simulations done in 2014 [2]
  Simulations were without intensity effects
  Limited consideration of measured beam parameters
The goal of the present study is to test slip-stacking feasibility with
  Full SPS impedance model
  Measured beam parameters
  Optimization with respect to the most significant parameters involved
[1] A. Saa Hernandez ‘Results from ion studies in PS & SPS from 2016/2017 and planning for 2018’, Injector MD day, 2018
[2] T. Argyropoulos et al. ‘Slip stacking in the SPS’, LIU Day, 2014

## Slide 5: Contents
Introduction
Slip-stacking fundamentals
Slip-stacking in SPS
Results for Q20 optics
  Parameter optimizations
  Suggested solution
Results for Q22 and Q26 optics
Conclusions and next steps

## Slide 6: Equations behind slip-stacking
Examples above transition (>0)
1 bunch
2 bunches
48 bunches

## Slide 7: RF perturbation
Unfortunately each RF system, while accelerates one batch, perturbs the other batch.
The perturbation is zero when the batch distance is greater than the time needed to switch alternatively the two RF systems on and off depending on which batch passes by.
The perturbation has less damaging effects when is large relative to
  the perturbation averages within a synchrotron oscillation period (no coherent effects)
It has been proven (F. E. Mills) that a lower limit for stable motion is defined by
is called slip-stacking parameter and two different cases with the same show in first approximation the same beam dynamics
    >> 4 -> small perturbation effect but large needed recapture voltage and large emittance after filamentation
    4 -> smaller recapture voltage needed (and small emittance growth after recapture ) but the perturbation has more effect
separatrices of the buckets of the two batches are tangent to each other
Difference in RF frequency between the 2 RF systems
Core synchrotron frequency
Half-bucket height
Difference in absolute energy
between the two batches

## Slide 8: Examples with RF perturbation
Example 2: -> perturbation is visible but bunch still inside bucket
Example 3: -> bunch is lost
Example 1: -> perturbation practically not visible
Bunches become red when perturbation starts

## Slide 9: Contents
Introduction
Slip-stacking fundamentals
Slip-stacking in SPS
Results for Q20 optics
  Parameter optimizations
  Suggested solution
Results for Q22 and Q26 optics
Conclusions and next steps

## Slide 10: Slip-stacking procedure in SPS
Two SPS batches, each batch contains 24 bunches spaced by 100 ns
Before slip-stacking the two batches are separated by = 2.7
  is defined by the LLRF specifications: it has to be so large that when = then to avoid perturbation from the other RF
  In SPS = 1.3 ( is the time needed to switch the RF system off)
Each batch is controlled by a different subset of the 200 MHz TWCs
Slip-stacking to make the two batches interleave
  Bunch spacing reduced from 100 ns to 50 ns
After slip-stacking:
  A common recapture voltage is needed
  Recapture done at the average (design) RF frequency

## Slide 11
Momentum program design
At which energy should slip-stacking be performed?
    Flat bottom: strong space charge effects, IBS and RF noise (observed during operation)
    Flat top: extra time for filamentation is needed and uncaptured beam is transfered to the LHC
    Intermediate energy plateau: weak space charge (but instability threshold ~ 1/E), presence of time for filamentation and cleaner beam for LHC
The energy 300 GeV/qc is chosen for the following simulations
Multiples of 1.2 s (PSB cycle) can be added to the SPS cycle for slip-stacking
  1.2 s are added at 300 GeV/c

## Slide 12
Slip-stacking programs
The momentum (or frequency) program is designed in such a way that the two batches are perfectly interleaved at
  Alignment has to be precise to avoid
additional filamentation after recapture
The voltage program is calculated from the momentum program for constant filling factor in energy
The batches move in opposite directions relative to , ,
Example of programs used in simulations for one of the two batches:
at

## Slide 13
Programs after slip-stacking
The capture voltage chosen at is used in [,], then the code computes the filling factor in energy at and uses it to calculate the voltage program in [,]
End slip-stacking
Capture voltage
Here filling factor is computed
with filling factor = 0.92
Example of in [,] encountered in simulations
At flat top two options are considered
  is increased linearly to 15 MV in 0.5 s (flat top length 1 s) (bunch compression)
  is constant for 0.8 s and then is increased non-adiabatically to 15 MV (bunch rotation)
We assume that the maximum available RF voltage is 15 MV
Start slip-stacking

## Slide 14
Initial beam parameters
Measurements done in December 2015 (courtesy A. Lasheen) show significant bunch to bunch variation in intensity and emittance along the batch at various point along the ramp
These beam parameters are exactly reproduced in simulations as starting point for the simulations
At 300 GeV/c
At 300 GeV/c
Intensity increases by a factor of 1.5
Emittance increases by a factor of 2

## Slide 15: Contents
Introduction
Slip-stacking fundamentals
Slip-stacking in SPS
Results for Q20 optics
  Parameter optimizations
  Suggested solution
Results for Q22 and Q26 optics
Conclusions and next steps

## Slide 16: Optimization of slip-stacking parameters
We define the total losses as
Constraints on
  %
  1.65 ns (maximum bunch length along the batch at SPS extraction)
We want to find the optimal combinations of parameters , and
  The dynamics are complex (many parameters involved, intensity effects, …)
  We don’t want to choose sub-optimal combinations for our proposals
Large parameter scan made possible by several algorithms which compute automatically for each case the design SPS programs
  scanned from 3.5 to 8, step 0.5
  scanned from 0.45 to 0.9, step 0.05
  scanned from 1 MV to 9 MV, step 0.5
We want also to monitor the maximum emittance along the batch at (after recapture filamentation)
Losses in SPS
Satellites in LHC

## Slide 17
Q20: no intensity effects, compression
Scan result
Optimal solutions
and [%]
Constraints are practically not satisfied
Behavior of main parameters for the optimal solutions

## Slide 18
Q20: intensity effects, compression
and [%]
No significant difference if intensity effects are on
Scan result
Optimal solutions
Behavior of main parameters for the optimal solutions

## Slide 19
Q20: no intensity effects, rotation
and [%]
Constraints are largely satisfied
Scan result
Optimal solutions
Behavior of main parameters for the optimal solutions

## Slide 20
Q20: intensity effects, rotation
and [%]
No significant difference if intensity effects are on
Optimal solutions
Scan result
Behavior of main parameters for the optimal solutions

## Slide 21
Parameters of the optimal solutions
All optimal solutions have roughly the same as expected
  Different configurations with same are similar from a slip-stacking perspective
, because 4 is the lower limit for stability and the solutions are optimal
  The results show that on average is preferable (some margin is due to the tails of the larger emittance bunches which approach the separatrix)
If we want for example lower , qualitatively it follows that
  decreases (lower bunch length for lower emittance bunch)
  decreases (filamentation after recapture fills the entire bucket, bucket area has to decrease)
  decreases (otherwise particles outside the recapture bucket will be lost)
  decreases ( is constant)
  increases (, )
  increases (bunch centroid closer to axis , stronger perturbations)
  increases (higher filling factor increases losses of particles close to separatrix)

## Slide 22
Q20: proposed solution S
    The results of the optimization shows that
      Intensity effects do not influence how the constraints are satisfied
      Bunch compression at flat-top cannot fullfill the requirements
      Bunch rotation at flat-top largely fullfils the requirements
    Giving priority to loss reduction
    we propose the combination with
and [%]
  %
  ns
  %
  %
  eVs/A
  MV
Low helps limiting considerably the losses in SPS during slip-stacking
Low and helps limiting influence of chaotic motion in making very low

## Slide 23
Q20: solution S, slip-stacking
Symbol | Units | Value
 | Hz | 139.3
 |  | 3x10-3
 | MV | 1.54
/ | - | 1.66x10-3
 | mm | 5.67
 | Hz | 1013
Symbol | Units | Value
 | Hz | 139.3
 |  | 3x10-3
 | MV | 1.54
 | - | 1.66x10-3
 | mm | 5.67
 | Hz | 1013
Parameters for one batch
RF voltage for one batch
for one batch and distance between batches (from head to head)
=4
=4.5
RF perturbation starts here,
=720
bunch distance after slip-stacking
Adiabaticity coefficient for one batch
=10
acceleration
deceleration
flat
[1/rad]

## Slide 24
Q20: solution S, after slip-stacking
Max RF voltage 14.62 MV
Momentum program
cycle time [s]
RF voltage [MV]
Adiabaticity coefficient
[1/rad]
RF program
At flat top, constant RF voltage for 0.8 s and then bunch rotation
[GeV/qc]
MOVIES for solution S: Initial bunch distributions for one batch
: bucket area, bunch length conventions, : # protons per bunch
: voltage induced by impedances and space charge

## Slide 25
MOVIES for solution S: slip-stacking
General frame, ,
Zoom on first two bunches
Bunches become red when RF perturbation starts
As expected only few particle lost during slip-stacking
At the end of slip-stacking low impact of chaotic motion in
Resonances visible at the end of slip-stacking and core which performes dipole oscillations

## Slide 26
MOVIES for solution S: capture and ramp
General frame
Bunches become yellow when the ramp starts
Few losses due to recapture and acceleration of higher emittance bunches
Small but very dense area in phase space never filaments (stronger for first bunch)
Middle bunch
First bunch
Last bunch

## Slide 27
MOVIES for solution S: flat top
General frame
The dense area never filaments
  Loss of Landau damping due to collective effects
  Without intensity effects immediate filamentation
First bunch
Middle bunch
Last bunch

## Slide 28
Loss of Landau damping
Loss of Landau damping when the second RF system perturbs the batch during slip-stacking
  Dipole oscillations stronger for shorter bunches inside the batch
Solution S without intensity effects, dipole oscillations damp
Solution S with intensity effects, large dipole oscillations never dump
Max mean position and rms of the first bunch at flat top along the optimal solutions (S is marked by green line)
  Dipole oscillations stronger for small
  Quadrupole oscillations smaller for small since the rotating island is very dense
First tests to damp these oscillations with the 800 MHz RF cavity gave negative results
Slip-stacking
Recapture and ramp
Flat top
RF perturbation starts here
Slip-stacking
Recapture and ramp
Flat top

## Slide 29: Contents
Introduction
Slip-stacking fundamentals
Slip-stacking in SPS
Results for Q20 optics
  Parameter optimizations
  Suggested solution
Results for Q22 and Q26 optics
Conclusions and next steps

## Slide 30
Q22: intensity effects, compression
and [%]
Acceptable margin for constraint fulfillment
Scan result
Optimal solutions
Behavior of main parameters for the optimal solutions
Fixed , lower lower lower more acceptable solutions

## Slide 31
Q22: intensity effects, rotation
and [%]
Scan result
Optimal solutions
Behavior of main parameters for the optimal solutions
Fixed , lower implies lower lower more acceptable solutions
Constraints are largely satisfied, even better than Q20

## Slide 32
Q26: intensity effects
Bunch compression
Bunch rotation
Constraints are largely satisfied, even better than Q22 (lower )
Constraints are largely satisfied, even better than Q22 (lower )
Scan result
Scan result
Optimal solutions
Optimal solutions

## Slide 33: Contents
Introduction
Slip-stacking fundamentals
Slip-stacking in SPS
Results for Q20 optics
  Parameter optimizations
  Suggested solution
Results for Q22 and Q26 optics
Conclusions and next steps

## Slide 34: Conclusions and next steps
The principle behind slip-stacking has been illustrated through different examples
The slip-stacking procedure has been simulated for the SPS-ion beams to verify its feasibility after LS2
  Many ring parameters were designed (voltage and RF programs during and outside the slip-stacking time, duration of the different cycle phases)
  Effort spent to use measured bunch distributions
  Realistic losses count mechanisms and machine parameters used
  The three different optics have been tested
  Full SPS impedance model included in simulations
Simulation results:
  Q20: bunch compression cannot satisfy constraints with enough margin, bunch rotation is needed
  Q22 and Q26: bunch compression can be used, even if bunch rotation gives always better results
Next step:
  Try counteracting loss of Landau damping through beam-based loops and the 800 MHz RF system