## Slide 1: SPS RF manipulations
G. Papotti
acks: T. Bohl, E. Shaposhnikova
LIU-SPS Beam Dynamics Working Group, 2019-03-28

## Slide 2: outline
introduce 3 manipulations:
  RF gymnastics by phase jump
  bunch rotation by non-adiabatic voltage step
  long/short debunching, recapture
focus on motivation & pre-LS2 implementation
  (specs for LIU-SPS RF LL under discussion)

## Slide 3: phase jump for Fixed Target
peak det
Vtot
inv ampli pol
motivation: slow extraction for pFT, iFT
  NA experiments need constant spill (during and across cycles)
  increase dp/p, flatten dp/p distribution, and debunch
manipulation sequence:
  phase jump to unstable phase
  jump back to standard, stable phase, after t1
    1. and 2. to increase and flatten dp/p
  turn RF off (after t2) for debunching
setting up
  optimize t1 for max peak (typ ~20 turns)
  adjust t2 to turn RF off at peak (typ ~2.3 ms)
hw: 360 deg phase discriminator + inverting ampli.
RF off
t1
t2

## Slide 4: non-adiab voltage step for pAWK
motivation: short bunch at extraction for AWK
  hw did not allow for phase jump
manipulation: non-adiabatic voltage step
  use pulse generator
    synchronized with extraction, thus AWAKE
    synch to frep, precision better than one turn
    risetime ~1 ms, amplitude Vtot = 7.8 MV
  lower voltage adiabatically first
    800 MHz needs to follow
OP needs to toggle back and forth
  trim voltage program & enable voltage pulse
  could see total voltage on Oasis, not in LSA
extract

## Slide 5: debunching, recapture
motivation: want a constant spill for iFT
  4 equidistant bunches, to uniformly distributed in buckets
manipulation sequence (at interm. flat top)
  turn RF off to allow debunching
  then RF on to recapture
OP to toggle 3 timings for debunching
  b-pulses off
  all RF off
  (ions prepare debunching, due to RFLL hw)
recapture is fixed and untouched by OP
  2 pairs of cavities at a time, 1 ms apart

## Slide 6: long vs short debunching
motivation:
  long debunching (ld): standard for physics operation
  short debunching (sd): for OP to setup the rest of the cycle (orbit, tune, …)
implementation
  change the same 3 timings, to different delays
  minimum differences in setup
post LS2: is “no debunching” an option?
RF off (ld)
RF off (sd)
RF on