## Slide 1: CERN-SPS horizontal instability
C. Zannini, H. Bartosik, M. Beck, T. Bohl, M. Carla’,
L.R. Carver, H. Damerau, V. Kain, G. Kotzian, A. Lasheen,
K. Li, E. Métral, G. Papotti, J. Repond, G. Rumolo, B. Salvant, M. Schenk, M. Schwarz, E. Shaposhnikova
SPS & PS operators

## Slide 2: Overview
What the transverse impedance model can explain in the SPS
Horizontal instability with multiple bunches
  Understanding of the SPS horizontal instability
    Sacherer theory
    PyHEADTAIL simulations
Summary

## Slide 3
Beam Dynamics Simulations
Determine effect on the beam
Machine Impedance model
Impedance as input of beam dynamics simulations
Analytical equation (e.g. Sacherer theory)
Vlasov Solver (e.g. DELPHI)
Macroparticle simulations (e.g. PyHEADTAIL)
Needed wake/impedance range depends on the specific beam dynamics under investigation
Driving Impedance
Driving and Detuning wake

## Slide 4: SPS transverse impedance model
Elements included in the database:
  Wall impedance that takes into account the different SPS vacuum chambers (analytical calculations)
  Kickers (CST 3D simulations)
  RF cavities (200 MHZ and 800 MHz) without couplers (CST 3D simulations)
  Broadband impedance of step transitions (CST 3D simulations)
  Horizontal (BPH) and vertical (BPV) beam position monitors (CST 3D simulations)
  Step-transitions and flanges (CST 3D simulations)
Kickers
Beam pipe
BPH
BPV
RF cavities
Step transitions

## Slide 5
SPS transverse impedance model

## Slide 6: SPS transverse impedance model
100 %
20 %
40 %
60 %
80 %
  Benchmark with beam measurements (coherent tune shifts, head-tail instability growth rates mode 0, TMCI thresholds and intra-bunch motion)

## Slide 7: SPS transverse impedance model
  Benchmark with beam measurements (coherent tune shifts, head-tail instability growth rates mode 0, TMCI thresholds and intra-bunch motion)

## Slide 8: SPS transverse impedance model
  Benchmark with beam measurements (coherent tune shifts, head-tail instability growth rates mode 0, TMCI thresholds and intra-bunch motion)
Q20 optics
Mode 0
Vertical

## Slide 9: SPS transverse impedance model
  Benchmark with beam measurements (coherent tune shifts, head-tail instability growth rates mode 0, TMCI thresholds and intra-bunch motion)
Q26 optics
Mode 0
Vertical

## Slide 10: SPS transverse impedance model
  Benchmark with beam measurements (coherent tune shifts, head-tail instability growth rates mode 0, TMCI thresholds and intra-bunch motion)
10
measurements
HEADTAIL simulations
4.5x1011 p/b
@ 0.35 eVs
nominal
Island of slow instability

## Slide 11: SPS transverse impedance model
  Benchmark with beam measurements (coherent tune shifts, head-tail instability growth rates mode 0, TMCI thresholds and intra-bunch motion)
11
measurements
HEADTAIL simulations
4.5x1011 p/b
@ 0.35 eVs
nominal
Island of slow instability

## Slide 12: Overview
What the transverse impedance model can explain in the SPS
Horizontal instability with multiple bunches
  Understanding of the SPS horizontal instability
    Sacherer theory
    PyHEADTAIL simulations
Summary

## Slide 13: Next challenge for the SPS impedance model: multi-bunch horizontal instability
2018 MDs observations
Stable with 1 batch at 2e11
Unstable with 4 batches at 2e11 with BS = 200ns
Mode1 or Mode2 instability depending on chroma
Stabilization at chromax about 0.6
Stabilization with batch spacing >500 ns
Some stabilization with octupoles
Instability threshold at about 1.8e11
ξH~0.1–0.2
ξH~0.3–0.5
Development of a dedicated model for multi-bunch simulations
Important to use analytical models to minimize numerical artefacts
  Stabilization above 2.1e11 ppb not evident during 2018 MDs

## Slide 14: SPS horizontal instability: observations
Mode 1
Mode 2
In 2017 the 4 x 48 bunches suffered from single bunch instabilities (some bunches in 3rd and 4th batch)
Chromaticity | Beam Stability
ξ=0.17 | Unstable mode1
ξ=0.27 | Unstable mode1
ξ=0.37 | Unstable mode1
ξ=0.47 | Unstable mode2
ξ=0.57 | Stable
ξ=0.67 | Stable
Summary of instability observations
L. R. Carver, Horizontal Instability During High Intensity Run
H. Bartosik et al., Summary from high intensity run (transverse), LIU-SPS-BD meeting, 19.10.2017
https://docs.google.com/presentation/d/1o2NMNl-Up7lwaYoNW3rgwHuA_-kosCByWSxxZ7C-6c0/edit#slide=id.g36dac49bd4_0_104

## Slide 15: Overview
What the transverse impedance model can explain in the SPS
Horizontal instability with multiple bunches
  Understanding of the SPS horizontal instability
    Sacherer theory
    PyHEADTAIL simulations
Summary

## Slide 16: SPS impedance model expectations
The MKE kicker model has been updated to consider the shortening of the serigraphy and the update of sector 4 (removal of one MKE-L)
year | MKE (incl. MKEser) | 200 mm serigraphy | 180 mm serigraphy
2006 | 9 | 0.5 | 0
2012 | 8 | 7 | 0
2015 | 8 | 8 | 0
2016 | 7 | 6 | 1
2017 | 7 | 3 | 4
2018 | 7 | 0 | 7

## Slide 17: Which is the driving term of the instability?
MKE with serigraphy
MKE without serigraphy
Effect of the serigraphy peak was first studied in 2007 by E. Métral and B. Salvant https://impedance.web.cern.ch/impedance/documents/UpdateOfSPSKickers_APC_27-04-07.pdf
The serigraphy peak was fitted with a resonator and it was concluded that the growth rate due to the resonance would have been significantly smaller than the one expected from wall impedance.

## Slide 18: Which is the driving term of the instability?
MKE with serigraphy
MKE without serigraphy
Impedance source: combination of wall and kicker impedance

## Slide 19: Only Wall Impedance
Vertical plane more unstable than horizontal
  vertical driving impedance is larger than horizontal driving impedance
Mode 1

## Slide 20: Wall and kicker without serigraphy
Instability at positive chromaticity stabilized by kickers
Horizontal plane more unstable for negative chromaticity and more stable for positive chromaticity
  higher horizontal dipolar kicker impedance
Mode 1

## Slide 21: Wall and kickers with serigraphy
Instability at positive chromaticity enhanced by kickers with serigraphy
  80 MHz resonance
  lower broadband stabilizing impedance
horizontal plane get more unstable than vertical plane
  higher 80 MHz peak
  lower broadband stabilizing impedance
Mode 1

## Slide 22: Full SPS model
BPMs, step-transitions, flanges and RF cavities seems to play a minor role in the headtail instability behaviour

## Slide 23
Impedance model | Beam Stability
Wall | UnstableY
Wall+kickers without serigraphy | Stable
Wall+kickers with serigraphy | UnstableX
Full model | UnstableX
The kicker broadband impedance has a stabilizing effect for modes l>0 and ξ>0.
The serigraphy enhances the wall instability
  80 MHz resonance
The serigraphy reduces the stabilizing effect of the kicker broadband impedance
  lower broadband impedance
Understanding of the SPS horizontal instability: Sacherer theory
Mode l>0 and ξ>0

## Slide 24
Chromaticity | Beam Stability
ξ=0.17 | Unstable mode1
ξ=0.27 | Unstable mode1
ξ=0.37 | Unstable mode1
ξ=0.47 | Unstable mode2
ξ=0.57 | Stable
ξ=0.67 | Stable
Summary of instability observations
Impedance source: combination of wall and kicker impedance
Understanding of the SPS horizontal instability: Sacherer theory

## Slide 25
The growth rates from impedance are expected to be almost unaffected by the serigraphy change
Understanding of the SPS horizontal instability: Sacherer theory

## Slide 26
Everything understood?
  Analytical studies do not take into account
    Arbitrary filling scheme
      Stability dependence on number of batches and batch spacing
    Effect of damper
    Effect of detuning impedance
    Nonlinearities
Understanding of the SPS horizontal instability: Sacherer theory

## Slide 27: Overview
What the transverse impedance model can explain in the SPS
Horizontal instability with multiple bunches
  Understanding of the SPS horizontal instability
    Sacherer theory
    PyHEADTAIL simulations
Summary

## Slide 28
2018 MDs observations
Stable with 1 batch at 2e11
Unstable with 4 batches at 2e11 with BS = 200ns
Mode1 or Mode2 instability depending on chroma
Stabilization at chromax about 0.6
Stabilization with batch spacing >500 ns
Some stabilization with octupoles
Instability threshold at about 1.8e11
ξH~0.1–0.2
ξH~0.3–0.5
Understanding of the SPS horizontal instability: 2018 measurement campaign
N=2e11 ppb
4x48 bunches, BS=200 ns
From headtail monitor measurements data

## Slide 29
Understanding of the SPS horizontal instability: 2018 measurement campaign

## Slide 30
PyHEADTAIL
Measurement
Horizontal
Vertical
Good agreement in the vertical plane
Impedance model: wall
Threshold effect in measurements not observed in simulations
Electron cloud effect?
Understanding of the SPS horizontal instability: PyHEADTAIL simulations

## Slide 31
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Stable with 1 batch unstable with 4 batches at 2e11, Stabilization with batch spacing,
Instability threshold around 1.8e11
One batch
4 batches
N=2.0e11 ppb
ξ=0.2

## Slide 32
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Stable with 1 batch unstable with 4 batches at 2e11, Stabilization with batch spacing,
Instability threshold around 1.8e11
One batch
4 batches
N=2.2e11 ppb
ξ=0.2

## Slide 33
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Stable with 1 batch unstable with 4 batches at 2e11, Stabilization with batch spacing,
Instability threshold around 1.8e11
200ns spacing
500ns spacing
N=2.2e11 ppb
ξ=0.2

## Slide 34
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Stable with 1 batch unstable with 4 batches at 2e11, Stabilization with batch spacing,
Instability threshold around 1.8e11
200ns spacing
1000ns spacing
N=2.2e11 ppb
ξ=0.2

## Slide 35
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Stable with 1 batch unstable with 4 batches at 2e11, Stabilization with batch spacing,
Instability threshold around 1.8e11
N=1.6e11 ppb
ξ=0.2

## Slide 36
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Stable with 1 batch unstable with 4 batches at 2e11, Stabilization with batch spacing,
Instability threshold around 1.8e11
N=2.0e11 ppb
N=2.2e11 ppb
ξ=0.2

## Slide 37
MD observations | Multibunch PyHEADTAIL simulations
Stable with 1 batch at 2e11 | ok
Unstable with 4 batches at 2e11 with BS = 200ns | ok
Mode1 or Mode2 instability depending on chroma | ongoing
Stabilization at chromax about 0.6 | ongoing
Stabilization with batch spacing >500 ns | ok
Some stabilization with octupoles | To be studied
Instability threshold at about 1.8e11 | Within 10% (ok)
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Studies still ongoing
It looks we are on the good way

## Slide 38: Some potential mitigation
Stabilization with octupoles, chroma and damper
  not obvious above 2.1e11 during the 2018 MDs
Impedance mitigation
  Modifying once again MKE serigraphy
    MKE serigraphy design is optimized to reduce beam induced heating whatever change will likely worsen the situation
Crazy solution: putting a stabilizing device
  MKE like structure
    The impedance will have a destabilizing effect for TMCI and longitudinal plane (equivalent to an increase of the kicker broadband impedance)
      Once simulation model is fully benchmarked we could be more quantitative on the impedance needed
Implement WBFS

## Slide 39: Summary
SPS horizontal instability could be a serious limitation for LIU
A possible explanation of the impedance mechanism driving the instability has been presented by using Sacherer theory
More involved model including arbitrary filling scheme, damper, detuning impedance and nonlinearities goes in the same direction
  To be continued
    Finalize the benchmarking studies
    Using the simulation model to study possible mitigation measures

## Slide 40: Thank you for your attention

## Slide 41: Appendix

## Slide 42: Headtail transverse instability
Mode 0 above transition is stable for positive chromaticity and unstable for negative chromaticity
  general rule for
Mode l>0 above transition are unstable for positive chromaticity and stable for negative chromaticity
  depends on the impedance

## Slide 43: Headtail mode 0
ξ=0.2
SPS wall impedance model

## Slide 44
Headtail mode l>0
SPS wall impedance model
No general rule for stability criteria can be given for mode 1
ξ=0.2

## Slide 45
Headtail mode l>0
SPS wall impedance model
No general rule for stability criteria can be given for mode 1

## Slide 46
Headtail mode l>0
SPS kicker impedance model without serigraphy
No general rule for stability criteria can be given for mode 1
ξ=0.2

## Slide 47
Headtail mode l>0
SPS kicker impedance model without serigraphy
No general rule for stability criteria can be given for mode 1

## Slide 48: Summary plot of the headtail growth rates with SPS model without serigraphy
Sacherer theory

## Slide 49: SPS growth rates with SPS impedance model from Sacherer theory
Mode 1
Mode 1
SPS impedance model (Sacherer theory)
SPS impedance model (Sacherer theory)
The instability could be enhanced with multiple bunches
M=1
M=48

## Slide 50: SPS transverse impedance model
  Benchmark with beam measurements (coherent tune shifts, head-tail instability growth rates mode 0, TMCI thresholds and intra-bunch motion)
Q20 optics
Mode 0
M. Beck et al., STUDIES OF HORIZONTAL INSTABILITIES IN THE CERN SPS, IPAC2018
Horizontal

## Slide 51: SPS headtail instability growth rates
Chromaticity | Beam Stability
ξ=0.17 | Unstable mode1
ξ=0.27 | Unstable mode1
ξ=0.37 | Unstable mode1
ξ=0.47 | Unstable mode2
ξ=0.57 | Stable
ξ=0.67 | Stable
Mode 1
Summary of instability observations
SPS impedance model (Sacherer theory)
M=1

## Slide 52: SPS headtail instability growth rates
Mode 2
SPS impedance model (Sacherer theory)
Chromaticity | Beam Stability
ξ=0.17 | Unstable mode1
ξ=0.27 | Unstable mode1
ξ=0.37 | Unstable mode1
ξ=0.47 | Unstable mode2
ξ=0.57 | Stable
ξ=0.67 | Stable
Summary of instability observations
M=1

## Slide 53: SPS headtail instability growth rates
Mode 3
SPS impedance model (Sacherer theory)
Chromaticity | Beam Stability
ξ=0.17 | Unstable mode1
ξ=0.27 | Unstable mode1
ξ=0.37 | Unstable mode1
ξ=0.47 | Unstable mode2
ξ=0.57 | Stable
ξ=0.67 | Stable
Summary of instability observations
M=1

## Slide 54: SPS headtail instability growth rates
Mode 1
Mode 1
SPS impedance model (Sacherer theory)
SPS impedance model (Sacherer theory)
Expectations from the SPS impedance model with Sacherer theory are consistent with instability observations
M=1
M=1

## Slide 55: Effect of wall and kicker impedance with and without detuning impedance
Impedance+Damper
Horizontal
Vertical

## Slide 56: SPS horizontal instability
If c), build and implement WBFS in H plane (>2 MCHF)
Gradually commission LIU beams
Beams can be produced up to SPS extraction within budgets
Need for Q22 or e-cloud limits high intensity operation
Horizontal instability for high intensity cannot be suppressed
If b), operational deployment of existing (V) system
2020-21
2022
LS3
2023
2024
YETS
YETS
EYETS
G. Rumolo