## Slide 1: Different FB methods and effect on instability threshold
M. Schwarz
LIU-SPS BD WG meeting, 19/09/19
Acknowledgements:
E. Shaposhnikova, BLonD dev team
Work in progress!

## Slide 2
Different feedback models
In previous multi-batch simulations, the feedback of the 200 MHz TWC was modeled by reducing Rshunt by 26dB
Model feedback of 200 MHz by
  Reduction of Rshunt by 26dB (yellow)
  Impedance reduction factor (green) → more impedance around 198 MHz and 202 MHz

## Slide 3
Setup for full impedance model simulations
Flat top, double RF V200=10MV (V800/V200=0.1), Q20
4x72 bunches with 1 Million macro-particles per bunch
Initial bunches were matched including intensity effects!
Multi-batch simulation possible thanks to BLonD-MPI (K. Iliakis, LIU-SPS BD WG meeting, 21/02/2019)
Bunch spacing 5 RF buckets (25ns), batch spacing 40 RF buckets (200ns)
Use full impedance model
  200 MHz feedback modeled by reducing Rshunt by 26dB
  200 MHz feedback modeled by impedance reduction factor
No phase loop
BLonD simulation parameters: Δf=44kHz, 64bins/RF bucket
Simulate 100 000k turns of flat top (2.3s)
Beam considered unstable if maximum relative amplitude spread exceeds 0.07:

## Slide 4
Thresholds for different feedback models
With impedance reduction factor, threshold is significantly higher, even though we have more impedance! (also observed by J. Repond)
Possible reason: Different voltage modulation due to different FB models leads to different bunch-by-bunch synchrotron frequency spread and changes Landau damping
-26dB x Rshunt
With

## Slide 5
Estimate of frequency spread
Beam is stable if the relative coherent frequency spread is larger than (one-fourth) of the synchrotron frequency shift:
Follow the idea of [E. Vogel, T. Bohl, U. Werhle, PRST-AB, 8, 102801 (2005)]
Relative coherent frequency spread given by
Synchrotron frequency of each bunch j given by
Here, for the voltage amplitude at bunch j, we use the ratio of the (extremum) of the induced voltage in bucket j and the main voltage (V200=10MV):
Synchrotron frequency spread calculated from impedance as

## Slide 6
Threshold for different FB models
vj with Rshunt reduced by 26dB
Unstable
in simulation
Unstable
by criterion

## Slide 7
Threshold for different FB models
vj with Rshunt reduced by 26dB
vj for impedance reduction factor
Unstable
in simulation
Stable in simulation
Unstable
by criterion
Frequency shift doubles when using impedance reduction factor, but so does coherent frequency spread → no conclusions can be drawn yet
Unstable
by criterion

## Slide 8
Summary
Work in progress!
Model 200 MHz TWC feedback by
  Reducing Rshunt
  Impedance reduction factor
Using gives more impedance around 200 MHz but yields a higher threshold!?
Possibly due to different voltage modulation and change in bunch-by-bunch synchrotron frequency spread?
First attempt inconclusive
Next step: use single particle model with uneven filling pattern to compute synchronous frequency shift [e.g. S. Prabhakar et al., pp 2022, PRL 2001]
Thank you for your attention!