## Slide 1: Update on 915 MHz HOM
M. Schwarz
LIU-SPS BD WG meeting, 19/12/19
Acknowledgements:
A. Farricker, I. Karpov, P. Kramer, E. Shaposhnikova, BLonD dev team

## Slide 2
Motivation 915 MHz HOM
The 915 MHz HOMs have high Q and large R/Q → long range wake field couples batches
Exact values for 915 MHz HOM are not known at present (Rsh, fr, Q) and are difficult to measure and simulate
CST simulations of 915 MHz HOM assuming open boundary conditions (P. Kramer, 19/10/24 LIU-SPS BD WG meeting) give twice larger Rsh than what is in present longitudinal impedance model
What is the impact of this ‘higher Rsh case’ on multi-batch stability?
How does the threshold change when HOM resonance frequency is at exact multiples of the revolution frequency?

## Slide 3
Simulation Parameters
Flat top, double RF V200=10MV, Q20
4x72 bunches with 1 Million macro-particles per bunch
V800/V200=0.16, including voltage limitation due to beam loading (relevant above 2.5e11 p/b)
Multi-batch simulation possible thanks to BLonD-MPI (K. Iliakis, LIU-SPS BD WG meeting, 21/02/2019)
Bunch spacing 5 RF buckets (25ns), batch spacing 40 RF buckets (200ns)
Using full SPS impedance model, in particular
  200 & 800 MHz TWC feedbacks modeled by reducing Rsh by 26dB
  different models for 915 MHz HOM (see next slide)
  no phase loop
BLonD simulation parameters: frequency resolution exactly frev
Initial bunches were matched including intensity effects!
Simulate 100 000k turns of flat top (2.3s)
Beam considered unstable if maximum relative bunch length spread exceeds 0.07:

## Slide 4
Models for 915MHz HOMs
lower Rsh: Rsh~2MΩ, Q~5k (in current longitudinal SPS impedance model)
higher Rsh (open boundary conditions): Rsh~5MΩ, Q~18k (see appendix for exact values)
worst case: higher Rsh model, where fr of the two modes at (nearly) integer multiples of frev (next slide)
random: each cavity HOM (4 3-sections, 2 4-sections) has fr randomly shifted by ±50kHz
‘higher Rsh model’ has larger Rsh, but reduced R/Q compared to ‘lower Rsh’ model
3MΩ estimate from fixed target beam (I. Karpov, LIU-SPS BD WG meeting)

## Slide 5
Effect of 915 MHz HOM frequency shift (V800/V200 = 0.10)
lower Rsh model: Rsh~2MΩ, Q~5k
higher Rsh model: Rsh~5MΩ, Q~18k
worst case
915 HOMs at ; nominal resonance frequency
  closest integer such that ; ;
  ; dashed lines are at multiples of
Shifting by ~ 15kHz (n=0, df=0.1) yields ‘worst case’ model with lowest threshold

## Slide 6
Thresholds, different 915 MHz HOM models

## Slide 7
Thresholds
4x72 bunches; V800/V200=0.16, including voltage limitation due to beam loading

## Slide 8
Summary
Next steps
On-going CST simulations of 200 MHz TWCs including terminations (load and Y-chamber) and correct lengths of feeder lines → simulate threshold once new ‘realistic’(?) model of 915 MHz HOM becomes available
Different models of 915 MHz HOM yield similar multi-batch threshold
Beam HL-LHC design values (2.4e11 p/b and 1.65 ns bunch length) is stable, but no margin for shorter bunches
Power limitation mainly due to 200 MHz TWC, and V800/V200 was kept at 16% → ratio V800/V200 could be increased to gain larger stability margin
Thank you for your attention!

## Slide 9
Appendix

## Slide 10
Values for 915MHz HOMs
3 section | higher Rsh | lower Rsh
fr / GHz | 913.7; 914.8 | 914.0; 914.8
R / kΩ | 798; 593 | 231.0, 231.6
Q | 18586; 15290 | 3000; 3000
R/Q / Ω | 43; 39 | 77
τ / μs | 6.5; 5.3 | 1.0; 1.0
BW / kHz | 155; 192 | 957; 958
4 section* | higher Rsh | lower Rsh
fr / GHz | 913.7; 914.8 | 914.0; 914.8
R / kΩ | 1064; 791 | 385.0, 386.0
Q | 18586; 15290 | 5000; 5000
R/Q / Ω | 57; 52 | 77
τ / μs | 6.5; 5.3 | 1.7; 1.7
BW / kHz | 155; 192 | 574; 575
*scaled

## Slide 11
Power limitation
Total voltage in a TWC (interaction length , series impedance , zero phase slip) for given power and beam current : [G. Dôme, CERN-SPS/ARF/77-11, 1977]
Beam current at frequency : , , : p/b, bunch spacing ns
Use binomial-μ distribution with bunch length and bunch spectrum
  Spectrum close to 1 at 200MHz and only mild dependence on bunch length
  Strong bunch length-dependence at 800MHz
Available power:
  4-section cavity: 1.6MW
  3-section cavity: 1.05MW
  800MHz TWC: 216kW (peak), 144kW (average)

## Slide 12
Power limitation, 200 MHz TWC
Total voltage (plot capped at 10MV)
Mild dependence on bunch length
10 MV can be obtained below 2.5e11 p/b
Voltage drops quickly above 2.5e11 p/b

## Slide 13
Power limitation, 800 MHz TWC
Total voltage for peak power (left) and average power (right)
Use when computing voltage from average power
Voltage primarily limited by limited average power

## Slide 14
Power limitation, voltage ratio
Plot ratio: min(V800) / min(10MV, V200)
Voltage ratio can be satisfied everywhere
cannot be fulfilled for small bunch length and intensities between 1.5 and 2.7e11 p/b
A ratio can only be fulfilled above 3.0e11 p/b, where is power-limited