## Slide 1: Update on the CERN-SPS horizontal instability studies
C. Zannini, S. Antipov, H. Bartosik, M. Beck, M. Carla’,
L.R. Carver, E. Métral, N. Mounet, G. Rumolo, B. Salvant, M. Schenk,
Thanks to: T. Bohl, H. Damerau, V. Kain, G. Kotzian, A. Lasheen,
K. Li, G. Papotti, J. Repond, M. Schwarz, E. Shaposhnikova
SPS & PS operators

## Slide 2: Multi-bunch horizontal instability
2018 MDs observations
Stable with 1 batch at 2e11
Unstable with 4 batches at 2e11 with BS = 200ns
Mode1 or Mode2 instability depending on chroma
Stabilization at chromax about 0.6
Stabilization with batch spacing >500 ns
Some stabilization with octupoles
Instability threshold at about 1.8e11
ξH~0.1–0.2
ξH~0.3–0.5
Development of a dedicated model for multi-bunch simulations
Important to use analytical models to minimize numerical artefacts
  Stabilization above 2.1e11 ppb not evident during 2018 MDs

## Slide 3: SPS horizontal instability: observations
Mode 1
Mode 2
In 2017 the 4 x 48 bunches suffered from single bunch instabilities (some bunches in 3rd and 4th batch)
Chromaticity | Beam Stability
ξ=0.17 | Unstable mode1
ξ=0.27 | Unstable mode1
ξ=0.37 | Unstable mode1
ξ=0.47 | Unstable mode2
ξ=0.57 | Stable
ξ=0.67 | Stable
Summary of instability observations
L. R. Carver, Horizontal Instability During High Intensity Run
H. Bartosik et al., Summary from high intensity run (transverse), LIU-SPS-BD meeting, 19.10.2017
https://docs.google.com/presentation/d/1o2NMNl-Up7lwaYoNW3rgwHuA_-kosCByWSxxZ7C-6c0/edit#slide=id.g36dac49bd4_0_104

## Slide 4
Chromaticity | Beam Stability
ξ=0.17 | Unstable mode1
ξ=0.27 | Unstable mode1
ξ=0.37 | Unstable mode1
ξ=0.47 | Unstable mode2
ξ=0.57 | Stable
ξ=0.67 | Stable
Summary of instability observations
Impedance source: combination of wall and kicker impedance
Understanding of the SPS horizontal instability: Sacherer theory

## Slide 5: Example of the CERN-SPS: DELPHI simulations
DELPHI Vlasov solver confirms the results obtained with Sacherer theory

## Slide 6
Everything understood?
  Analytical studies do not take into account
    Actual filling scheme
      Stability dependence on number of batches and batch spacing
    Effect of damper
    Effect of detuning impedance
    Nonlinearities
Understanding of the SPS horizontal instability: Sacherer theory

## Slide 7
2018 MDs observations
Stable with 1 batch at 2e11
Unstable with 4 batches at 2e11 with BS = 200ns
Mode1 or Mode2 instability depending on chroma
Stabilization at chromax about 0.6
Stabilization with batch spacing >500 ns
Some stabilization with octupoles
Instability threshold at about 1.8e11
ξH~0.1–0.2
ξH~0.3–0.5
Understanding of the SPS horizontal instability: 2018 measurement campaign
N=2e11 ppb
4x48 bunches, BS=200 ns
From headtail monitor measurements data

## Slide 8
Understanding of the SPS horizontal instability: 2018 measurement campaign
Instability starts from the last batch and extend to the other batches for more critical settings

## Slide 9
MD observations | Multibunch PyHEADTAIL simulations
Stable with 1 batch at 2e11 | ok
Unstable with 4 batches at 2e11 with BS = 200ns | ok
Instability behaviour along the batches | ok
Stabilization with batch spacing >500 ns | ok
Instability threshold at about 1.8e11 | Within 10% (ok)
Stabilization at chromax about 0.6 | ongoing
Behaviour with chroma and octupoles | To be studied
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations

## Slide 10
MD observations | Multibunch PyHEADTAIL simulations
Stable with 1 batch at 2e11 | ok
Unstable with 4 batches at 2e11 with BS = 200ns | ok
Instability behaviour along the batches | ok
Stabilization with batch spacing >500 ns | ok
Instability threshold at about 1.8e11 | Within 10% (ok)
Stabilization at chromax about 0.6 | ok
Behaviour with chroma and octupoles | ok
Impedance model: wall and kickers
Kicker model fitted with resonators
Understanding of the SPS horizontal instability: PyHEADTAIL simulations
Improved kicker wake for multi-bunch range

## Slide 11: Instability versus chroma and octupoles: comparing measurements and simulations
Measurements
PyHEADTAIL simulations
Simulation can reproduce behaviour of the instability with chromaticity and octupoles
N=1.8e11 ppb

## Slide 12: Simulations at higher intensity
Stabilization is expected to be possible for reasonable settings of chromaticity and octupoles
N=2.3e11 ppb
4 x 48 bunches
Stable in measurements up to N=2.2e11 ppb
Preliminary

## Slide 13: Simulations at LIU intensity
At 2.6e11 for BCMS (4 x 48) a violent vertical instability is observed
With nominal beam the instability is observed already at 2.3e11
Preliminary

## Slide 14
PyHEADTAIL
Measurement
Horizontal
Vertical
Good agreement in the vertical plane
Impedance model: wall
Threshold effect in measurements not observed in simulations
Electron cloud effect?
Understanding of the SPS horizontal instability: PyHEADTAIL simulations

## Slide 15: Summary
SPS horizontal instability could be a serious limitation for LIU
A possible explanation of the impedance mechanism driving the instability has been presented by using Sacherer theory
More involved model including actual filling scheme, damper, detuning impedance and nonlinearities shows
  Behaviour versus octupoles and chromaticity of the instability successfully reproduced for BCMS 1.8e11 ppb
  Stabilization with octupoles, chroma and damper checked up to 2.3e11 ppb for BCMS beam (ξx=0.4, klof=-6.2)
Issues to be further investigated
  In simulations with high intensity (close to the LIU intensity) a violent vertical instability is observed
  Transverse emittance blow-up for stable points when using octupoles
  Beam lifetime and quality for the explored operational settings

## Slide 16: Thank you for your attention

## Slide 17: Appendix

## Slide 18: Impedance reduction is not always beneficial
Effect on the stability of the Headtail mode 1

## Slide 19: Headtail mode 0
ξ=0.2
SPS wall impedance model

## Slide 20
Headtail mode 1
SPS wall impedance model
No general rule for stability criteria can be given for mode 1
ξ=0.2
SPS kicker impedance model without serigraphy
ξ=0.2
For a given chromatic shift the sign of the effective impedance depends on the impedance type

## Slide 21: Wall Impedance
Headtail mode 1 above transition is unstable for positive chromaticity and stable for negative chromaticity
ξmax

## Slide 22: Ferrite loaded kickers impedance
Headtail mode 1 above transition is stable for positive chromaticity and unstable for negative chromaticity

## Slide 23: Interplay of impedances
The overall effect of different impedance contributions depends on the weight of stabilizing and destabilizing effects
Stabilizing
Destabilizing

## Slide 24: Interplay of impedances
The overall effect of different impedance contributions depends on the weight of stabilizing and destabilizing effects

## Slide 25: Interplay of impedances
The overall effect of different impedance contributions depends on the weight of stabilizing and destabilizing effects
An inductive impedance has a stabilizing effect for mode 1 and ξ>0.
  Reducing this kind of impedance makes the situation worst

## Slide 26: Example of the CERN-SPS
MKE with serigraphy
MKE without serigraphy

## Slide 27: Example of the CERN-SPS
Mode 1
Instability at positive chromaticity stabilized by kickers

## Slide 28: Example of the CERN-SPS
Instability at positive chromaticity enhanced by kickers with serigraphy
  80 MHz serigraphy resonance
  lower broadband stabilizing impedance
Mode 1

## Slide 29: Example of the CERN-SPS
Mode 1
A deep understanding of all the impedance induced effects is needed to make the best choice in terms of impedance optimization looking at both local (direct effect on the device) and global effects (interplay between the different impedances)

## Slide 30: Effect of wall and kicker impedance with and without detuning impedance
Impedance+Damper
Horizontal
Vertical