## Slide 1: Multipactor test stand Srgio Calatroni, Fritz Caspers, Pedro Costa Pinto, Luigi Leggiero, Mauro Taborelli
Goal of this meeting:
define the characteristics the system must have
Assign tasks (Fritz for the RF electronics, VSC for the rest)
Decide about the manpower to operate it. Workload enough for a diploma thesis. Check radiation issues. (take one of the two Germans).
Date estimated to have the system assembled: end November 2010.

## Slide 2: Multipactor test stand
define the characteristics the system must have
General orientation:
is it realistic try to reproduce the multipacting conditions we have in the SPS? (the same electron current, repetition rates, electron energies…)
Or shall we just have controlled multipacting to characterize the SEY?

## Slide 3: Multipactor test stand
define the characteristics the system must have
RF part:
insert the wire without scratching the central part of the chamber;
stretch it with a controlled and reproducible sag; (dynometer, RF)
Current feedthrough at one extremity, isolation at the other;
Adjustable DC bias for the wire; possibility of current measurement. (C’est Fritz qui regarde!)
Microwave antennas to measure e-cloud? Yes, flanges.
Electronics: Fritz qui regarde.

## Slide 4: Multipactor test stand
define the characteristics the system must have
vacuum part:
The dipole’s chamber is pumped through a known conductance; the pressure range in the dipole must be 10-8 to the 10-5 mbar;
A differentially pumped system will allow to work with the RGA in the range 10-10 to the 10-7 mbar;
The relaxation time of the differential system must be much smaller than the one of the chamber system;
Injection of gases in the chamber side to calibrate the RGA (H2, CO,…)
“exotic” options: possibility to pump the dipole with an ion pump equivalent to the SPS ones? NOT FOR THE FIRST PHASE
Possibility to do glow discharge cleaning
Water cooling for Idipole>400A (to be checked)
System to be installed in 867? Check space availability with Jeremie.