## Slide 1: SPSU Beam diagnostics for future SPS beams
The 2 Phases
Beam Position
Beam Intensity
Beam Transverse Dimensions
Beam Losses
Conclusions

## Slide 2: The 2 Phases Phases, BPM, BCT, BWS/BGI, BLM, Conclusions
Based on Elena’s suggestion, I’ll consider the 2 following cases for each instrument:
  PHASE 1: related to ultimate LHC intensity in the SPS, i.e. 1.7 10^11 p per bunch, 5 10^13 per beam, all other parameters stay the same.
  PHASE 2: SPS operation with PS2 as injector, based on the given FT/CNGS/LHC beam parameters

## Slide 3: The 2 Phases Phases, BPM, BCT, BWS/BGI, BLM, Conclusions
For PHASE 2, we will use the following extremes:
  Total Intensity: Max 13.4 10^13 p (factor 3) – Min 2.10^9 p
  Bunch Intensity: Max 5.0 10^11 p (factor 5) – Min 2.10^9 p
  Beam Sizes: Smallest 3/3 um
  Bunch Pattern: 40 MHz (only???)

## Slide 4: Beam Position Measurement Phases, BPM, BCT, BWS/BGI, BLM, Conclusions
Phase I:
  The current MOPOS system should have the same performance as today with 1.7 10^11p per bunch.
  But it already suffers from some issues with the different bunch spacing and large bunch intensities (offsets).
  We are currently working on
    Understanding the problem
    Replacing the current system with 2012 SU as target for commissioning. This project is approved and covered by SPS renovation project.
Phase 2:
  The new system can now include Phase 2 requirements if it is confirmed it has to.

## Slide 5: The Current Monitors Phases, BPM, BCT, BWS/BGI, BLM, Conclusions
Phase I:
  The DC and fast BCTs are ready for Phase 1 LHC ultimate beams
Phase 2:
  The DC and fast BCTs will need an upgrade to cope with PHASE 2 intensities
  Our current plan is to have the new BCT systems ready for commissioning for 2012 SU (to cope with ions in NA61).
  The new system can now include Phase 2 requirements if it is confirmed it has to.
  This still has to be funded (400 kCHF for the 3 monitors, including human safety issues).

## Slide 6: The Transverse Profile Monitors Phases, BPM, BCT, BWS/BGI, BLM, Conclusions
Phase I:
    The current BWS are ready for Phase 1 LHC ultimate beams
    We plan to upgrade and standardize their electronics during 2010/11 shutdown.
Phase 2:
  The current BWS will not withstand these intensities
  We are working on new fast wire scanners. Our current plan is to have a new BWS ready for 2014 SU which could be targeted for PS, SPS or LHC. TBD.
  The new system can now include Phase 2 requirements if it is confirmed it has to.
  This is still to be estimated and funded based on the results. Currently, we only have money for a laboratory prototype.
  We should also be able to work again on the SPS BGIs from 2010 onwards which should work under these conditions.

## Slide 7: The Beam Loss Monitors Phases, BPM, BCT, BWS/BGI, BLM, Conclusions
Phase I:
  The current BLM system should have the same performance as today with Phase I beams.
  We are currently working on its replacement on the PS complex with 2012 SU as target for commissioning. This project is currently covered for PS assuming that we will be able to reuse our current cables on same locations.
Phase 2:
  Our plan is to also deploy this new system on SPS but this will have to be estimated and funded
  The new system will be based on requirements (number and location of channels, sensitivity/integration time, response time…) that we just received from the users.

## Slide 8: Conclusions Phases, BPM, BCT, BWS/BGI, BLM, Conclusions
Phase I:
  We should be ready for phase 1 if current MOPOS weaknesses are acceptable.
Phase 2:
  A lot of work for SPS operation with PS2 as injector :
    Part of it is already in our pipeline, including budget
    The rest seems in our plans already but with no budget yet
  We should cross-check our timescales. Do you foresee any Phase 1.a,b,c?
  The impact on LHC BI systems to cope with these beam intensities is still to be estimated. Same applies for PS2 to SPS transfer line.