## Slide 1: MDs for 2011
SPSU SG meeting
16 December 2010

## Slide 2: Proposed MD studies/requests for 2011
re-establish low-loss nominal 25 ns beam, reference measurements for e-cloud (scrubbing?)
- 1st MD of 16 hours minimum (4h OP + 8h RF + 4h)
- Note, 75 ns and 50 ns nominal beams will be operational before 1st MD
limitations with “above nominal” intensity beams, increase of intensity in steps with time for optimisation
  probably 50 ns first and then 25 ns beam
  – each MD block, 12 hours minimum
transverse emittance preservation:
  accurate and systematic measurements during each MD
  minimisation of blow-up
  origin if blow-up unavoidable
impedance identification (transverse + HOM longitudinal)
  transverse – parallel MDs
  longitudinal - with 75 ns, 50 ns and 25 ns beam of variable (low) intensity
TMCI – single bunch - parallel MDs
  threshold in a double RF system
  multi-bunch stability
double RF system (stability and emittance blow-up) – nominal LHC beam

## Slide 3: Proposed MD studies/requests for 2011
Low gamma transition - most urgent studies
  optics studies - parallel MDs
  acceleration of nominal LHC beams late - long dedicated MD session(s)
    study minimum longitudinal emittance/bunch length at 450 GeV/c sufficient for beam stability

## Slide 4: RF issues for low γt
Successful MDs with a single bunch (H. Bartosik, Y. Papaphilippou et al.): γt=22.8 → 18, η increase 2.86 (26 GeV/c) to 1.6 (450 GeV/c)
Expected increase in beam stability for the same bunch parameters Nth~ η for both TMCI (observed!) and longitudinal instabilities
To have the same longitudinal parameters (bucket area) V ~ η → can be a problem for extraction to LHC of the same longitudinal emittance as now (now 4σ bunch length limit is 1.7 ns)
But emittance blow-up for the same stability in the SPS can be reduced: for loss of Landau damping Nth~ ε2 η τ. Since τ ~ (ε2 η/V)1/4
→ ε ~ η-1/2 and τ = const for V=const.
If LHC itself needs higher longitudinal emittance at injection (IBS, stability) → 200 MHz RF system in LHC?
Fast cycles are not possible (3 s or 4.2 s acceleration time)
Space charge limit, e-cloud - ?

## Slide 5: Voltage
γt = 19.6
γt = 22.8

## Slide 6: Loss of Landau damping single 200 MHZ RF system
γt=22.8
γt=19.6