## Slide 1: Electron cloud simulations for the SPS electrostatic septum (ZS) G. Rumolo, for the joint SPSU ST and TF meeting (22/04/2010)
Introduction and motivations
  Behaviour of ZS with LHC type beams
Study of electron cloud build up thresholds in a ZS-like geometry with LHC25 beams:
  Without external fields
  With the voltage from the ion traps
  With a solenoid field
Conclusions
 Inspired by many individual discussions with G. Arduini, B. Bahlan, B. Goddard, E. Métral...

## Slide 2: What the ZS looks like….

## Slide 3: Some practical information on the ZS
-220kV
-6kV
-3kV
Anode
Cathode
Ion-traps
Active length ~ 3 m (per septum).
Anode (grounded) :
  Equipped with 2000 W.75Re.25 septum wires.
  Wire diameter 50 mm (first ZS) to 100 mm.
  Wire spacing 1.5 mm.
Cathode at a voltage of -220 kV (110 kV/cm).
Anode-cathode gap : 20 mm.
Ion traps (circulating beam side):
  Voltage of -3 to -6.5 kV
  ~ 2-3 kV diff. top/bottom
  Sum of all voltage difference should be ~ 0 to avoid orbit distortions at low energy. Critical for leptons, usefulness less evident now…
From J. Wenninger, Introduction to Slow Extraction to the North Targets

## Slide 4: ZS during SPS operation with high intensity LHC beams
Following the 2002 incident with the ZS, operation still applies these instructions when high intensity LHC beams are in the SPS:
  retracted girder (maybe not in the future to allow cleaning)
  HV 0 kV;
  ion traps on;
Observations at the ZS with 25 ns high intensity beam:
  Above certain intensities (nominal beam, more than 1 batch injected) the vacuum in the ZS degrades.
  The increased vacuum levels can provoke a vacuum interlock, which stops the ion traps and hence the beam in the machine. In this sense, “ZS limits the LHC beam”.
  By increasing the bunch length the vacuum recovers again.
  The beam has a non-negligible effect on the ion trap voltages, as the ion trap voltage drops and current is drawn off the plates.
  Sparking does occasionally occur, but does not appear to be the principal problem
All this above suggests that we have e-cloud in the ZS, even if the presence of a voltage should clear from electrons….

## Slide 5: Electron cloud simulations (I) the ZS geometry without external fields
In absence of voltage from the ion traps
  significant electron cloud builds up for dmax > 1.7
  the electron cloud between bunches is uniformly distributed over the chamber cross section
46 mm
140 mm
lec = 1010 e-/m

## Slide 6: Electron cloud simulations (II) including the voltage from the ion traps
Assuming a voltage of 3 kV between the bottom and top plates
  the electron cloud is suppressed at least up to dmax =2.0
  actually electron clearing happens between bunches and there is no dependence on the SEY of the plate. A certain number of electrons survives between bunches, and also between batches, but it tends to saturate.
46 mm
140 mm
E
lec = 105 e-/m

## Slide 7: Electron cloud simulations (III) scanning the voltage values
Assuming dmax =2.0 and scanning the voltage between the bottom and top plate
  the electron cloud is found to be suppressed at for 500 V ≤ V < 4 kV
  V=100 V is not sufficient and a strong electron cloud is formed
  For V=100 V the SEY threshold lies between 1.6 and 1.7, and the electron cloud that builds up is stronger than in absence of voltage.

## Slide 8: Electron cloud simulations (IV) scanning the voltage values
When we change the voltage, we actually change the clearing efficiency
  electrons are cleared more efficiently (i.e. more quickly) with higher voltages
  However, if the voltage becomes
    too low (<500 V), no clearing happens and the voltage actually gives the electrons the additional energy as to slightly enhance the multipacting that would anyway occur without voltage applied
    too high (>7 kV), some electrons can be accelerated to high enough energies as to multiply their number when hitting the plate during/after a bunch passage
  the quoted clearing voltage values also depend on having assumed in the model a maximum SEY at Emax=230 eV

## Slide 9: Electron cloud simulations (V) distribution of electrons with clearing voltage
Distribution of electrons inside the beam chamber (snapshot taken just before the passage of the last bunch of the second batch):
  A certain concentration of electrons remains in the vicinity of the plate at higher potential (the higher the voltage, the more localized is the distribution)
  The amount probably also depends on the model assumption of 0.7 probability of elastic reflection at low energy!
x (cm)
y (cm)

## Slide 10: Electron cloud simulations (VI) effect of a solenoid field alone
Assuming a solenoid field of 50G and zero voltage
  The electron cloud is efficiently suppressed for dmax at least up to 2.0
  A certain number of electrons survives between bunches, and also between batches, but it tends to saturate
140 mm
B
46 mm
lec = 105 e-/m

## Slide 11: Electron cloud simulations (VII) scanning the value of the solenoid field
We have scanned the intensity of the solenoid field between 10G to 110G with dmax=2.0 and zero voltage
  Electron cloud suppression is efficient for all values, except B=10G
  Best suppression seems to be reached for B=30G

## Slide 12: Electron cloud simulations (VIII) distribution of electrons with solenoid
Distribution of electrons inside the beam chamber with zero voltage:
  For B=0, the electrons fill the beam chamber uniformly (red dots), while, due to the cyclotron motion of the electrons around the field lines, a solenoid makes secondary emission “inefficient”, as the emitted electrons bend back into the wall
  The same line density as with clearing voltage translates into a lower electron volume density due to the larger cross section occupied (however, in this case there would be a higher central density!)
y (cm)
x (cm)

## Slide 13: Electron cloud simulations (IX) voltage + solenoid
The presence of a solenoid field with a voltage of 3 kV seems to enhance the electron production, partially removing the suppressing effect that both separately have
  For B=50G, some spikes are created in the electron distribution vs. time
  For B=110G, a more stationary cloud of electrons is created and survives through bunches
140 mm
B
46 mm
E
lec = 108 e-/m

## Slide 14: Electron cloud simulations (X) voltage + solenoid
We try to understand the reason of this behaviour
  While the voltage alone can clear the electrons created by a bunch, the solenoid allows the electrons to gain more energy before they get to the wall, causing a “single bunch multipacting” (similar to trailing edge multipacting)
  For B=50G, these electrons are more or less cleared by the arrival of the next bunch
  For B=110G this effect persists through bunches giving rise to a significant cloud

## Slide 15: Electron cloud simulations (XI) distribution of electrons with voltage + solenoid
Distribution of electrons inside the beam chamber:
  As predictable, both with and without solenoid field the electrons accumulate in the vicinity of the plate at higher potential
  We can observe that the distribution with solenoid field shifts leftwards and extends more on the left side, possibly as an effect of the E x B drift.
Zoom on the electrons!

## Slide 16: Summary and conclusions
The geometry of the ZS is prone to electron cloud build up with LHC25 beams at nominal intensity
  in absence of the voltage from the ion traps, there would be electron cloud for maximum SEY above 1.7
A difference of potential between top and bottom plate should be effective to clear the electrons from residual gas ionization between bunches
  voltage should be at least a few hundreds V (100V certainly not enough)
  voltage should also be below ~7kV in order not to produce important single bunch electron multiplication
A solenoid field above 10G can also suppress the electron cloud in the ZS in absence of the clearing voltage
The combined effect of voltage and solenoid field can give rise to substantive electron cloud formation through the processes of single bunch multiplication and electron survival across bunches
Disclaimer: in all the study presented, no dynamic effects have been taken into account (e.g. voltage drop due to the passage of the beam, possible voltage change at the plates due to electron emission, etc.). It would be important to quantify the voltage change with passing beam