## Slide 1
Preliminary results and ideas for the SPS upgrade MDs on LHC beams in 2011
G. Rumolo on behalf of all the MD team (Elena, Thomas, Karel, Christina, Holger, Bettina, Heiko, Wolfgang, Daniel, Juan, Theodoros, the SPS operation crew, etc.)
Low gamma transition studies can be commented in detail by Hannes, Yannis, Benoît
Preliminary from the 1st long MD block (nominal 25ns beam, 50ns beams in single and double batch)

## Slide 2
We started parallel MDs in week 17
  Preparation for the LHC MDs (week 18) and long injector MD block (week 19)
  Longitudinal emittance blow up
  Instabilities at flat top related to radial steering
  Low gamma transition
Long MD block in Week 19 split around the technical stop

## Slide 3
Low gamma transition studies (Q20) were planned to start with single bunch on a parallel MD1 cycle (no acceleration) or LHCFAST (fast ramp to 450 GeV/c)
However, in order not to have to optimize twice the set up of this beam along the ramp, it was decided to use a 1-inj cycle with slow ramp, instead of the LHCFAST (9bp instead of the 6bp of the fast ramping cycle)

## Slide 4
So far, single bunches studies done on Q20 with intensities up to 3 x1011 and very low transverse emittances (~1 mm in both transverse planes)
The idea was to
  do the set up and study transmission on the short cycle
  explore beam behavior (i.e. loss and emittance growth) on a long flat bottom and over the long cycle as a function of the injected intensities and emittances

## Slide 5
Long MD block in Week 19 (Monday):
  Monday daytime: Set up of the 25ns beam (longitudinal parameters, transverse feedback system)
  Monday night: supercycle composed of two concurrent long flat bottom cycles, one for the 25ns beam and the other one for Q20 with single bunch
Injection and acceleration of 4 batches with losses down to 3-4%
Injection and acceleration of single bunch of up to 3 x 1011 protons: small loss on the flat bottom and capture loss

## Slide 6
MD with 25ns beam (1):
  Nominal intensity
    Up to 4 batches injected
    Very low losses along the cycle (reproducible 3-4%)

## Slide 7
MD with 25ns beam (2):
  Nominal intensity
    Emittances measured in the PSB and the PS
      PSB Eh=2.9 mm, Ev=2.0 mm averaged over the 4 rings (further optimization could be done)
      PS (different from different WSs, ignored FWS54H and averaged readings from the others): Eh=2.9 mm, Ev= 1.5 mm
    Emittances consistently measured in the SPS at every injection step
    Remarkably low emittances measured at flat top in the SPS:
      Eh=2.4 mm
      Ev=2.7 mm

## Slide 8
MD with 25ns beam (3):
  Electron cloud measured at all the liners
    Signal already visible with 1 batch on both stainless liners
    No signal visible on the a-C coating liner
    Half signal clearly visible on the half coated chamber
    Effect of the clearing electrode checked scanning points on a grid of voltage vs. magnetic field values
Clearing electrode: it was switched off in the middle of cycle
Half-coated liner, only stripe on StSt visible

## Slide 9
MD with 25ns beam (4):
  Problems:
    ZS had two vacuum spikes, even with the voltage applied, as from last year
    MKE heating: MKE4 (Tank 5) reached 70oC and interlocked the beam (4 minutes stop, then Q20 re-started, while we waited longer for the 25ns beam, which we anyway stopped accelerating)

## Slide 10
Long MD block in Week 19 (Wednesday):
  Wednesday daytime:
    MD started as scheduled at 8:00am thanks to Karel & operation crew, who did the re-alignment after the quadrupole exchange during the night!
    50ns double batch (1.4 x 1011 ppb at flat top) in the first part
    50ns double batch (close to 1.7 x 1011 ppb at flat top) in the second part
Injection and acceleration of 4 batches with losses less than 3%
Injection and acceleration of single bunch of up to 3 x 1011 protons: small loss on the flat bottom and capture loss

## Slide 11
Long MD block in Week 19 (Wednesday):
  Wednesday night:
    The switch to the 50ns single batch happened during the night due to a ~5h stop of the MD in the afternoon, caused by a Linac intervention (urgent replacement of a sparking RF modulator)
    50ns single batch (1.2 x 1011 ppb at flat top, nominal) in the first part
    50ns single batch (close to 1.45 x 1011 ppb at flat top) in the second part
Injection and acceleration of 4 batches with losses less than 3%, later optimized to less than 2%
Injection and acceleration of single bunch of up to 3 x 1011 protons: small loss on the flat bottom and capture loss

## Slide 12
MD with 50ns double batch beam (1):
  Intensity higher than nominal (we were initially deceived by the fastBCT, which is not correctly calibrated for 50ns beams)
    Up to 4 batches injected
    Very low losses along the cycle (reproducible 3%)

## Slide 13
MD with 50ns double batch beam (2):
  1.4 x 1011 ppb at flat top
    Emittances consistently measured in the SPS at every injection step
    Emittances always measured both at injection (after the last injection) and at flat top in the SPS and no emittance growth observable
    Emittances at flat top, clean beam shape:
      Eh=1.7 mm
      Ev=1.7 mm

## Slide 14
MD with 50ns double batch beam (3):
  Electron cloud measured at all the liners
    Signal already visible with 1 batch only on the stainless liner without clearing electrode!
    No signal visible on the a-C coating liner
    No signal visible on the half coated chamber (was in since last year)
    The two StSt liners were installed at same time (January 2011), why did we scrub more the one with the clearing electrode?
      More efficient scrubbing from high energy electrons/ions?
      Baking from beam induced heating??
StSt not yet scrubbed below 1.7 (expected threshold for 50ns beams)
Scrubbed StSt with clearing electrode
Great job from the VSC team that exchanged the quadrupole in LSS5 during TS, as no surface degradation is visible!!!!

## Slide 15
MD with 50ns double batch beam (4):
  Very close to ultimate intensity 1.65 x 1011 ppb at flat top
    Heiko in the PS used the 3 x 80 MHz cavities to increase/decrease the longitudinal blow up before injection into the SPS
    Found an intermediate configuration, which would not worsen capture losses and also keep the beam stable in the SPS, since the longitudinal blow up in the SPS with band-limited noise could not be optimized quickly (subject of one of next MDs)
    We had to increase the horizontal chromaticity by 0.1 to avoid losses

## Slide 16
MD with 50ns double batch beam (5):
  Very close to ultimate intensity 1.65 x 1011 ppb at flat top
    Higher e-cloud signal  (to be checked by Christina in off-line analysis)
    Small emittances measured across the injection chain
      PSB: Eh+Ev ranging between 2.5 and 3.2 mm (bad values in Ring1)
      PS: Eh + Ev=3.5 mm (smaller in vertical)
      SPS: Eh= 1.6 mm and Ev=1.9 mm at injection (sum 3.5)
      Eh=2.0 mm and Ev=1.9 mm at flat top (sum 3.9)

## Slide 17
MD with 50ns single batch beam (1):
  Nominal intensity 1.2 x 1011 to 1.45 x 1011 ppb at flat top
    Beam off-centered  the electron cloud shows only one stripe!
      The center of the beam pipe is much better scrubbed??
    Very low losses (below 3%)
    Emittances 3 mm in both planes at flat top

## Slide 18
MD with 50ns beams:
  No vacuum limitations (kicker outgassing, ZS sparking)
  No significant temperature rise of the kickers, although at the end of the MD a clear heating of MKE4 was found