## Slide 1: Short and preliminary summary of MD w19
MD participants: T. Argyropolous, H. Bartosik, C. Bhat, T. Bohl, W. Hofle, J. Esteban Muller, H. Neupert, Y. Papaphilippou, G. Rumolo, B. Salvant, E. Shaposhnikova, D. Valuch, C. Yin Vallgren + H. Damerau (PS)
plus help from G. Hagmann, U. Wehrle and OP shifts

## Slide 2: Main MD topics
25 ns nominal beam
50 ns beam
  higher than nominal bunch intensity (1.4→1.6 x1011)
  PS/SPS beam transfer for increased injected long. emittance with 2&3 the PS 80 MHz cavities during bunch rotation
  DB and SB production (low and higher tr. emit.)
Low γt (Q20) cycle in parallel to nominal optics cycle
  setting-up of long (nominal) cycle with corresponding voltage program
  (very) high intensity single bunch
  transverse emittance and losses for dif. intensities

## Slide 3: 25 ns nominal beam (Monday 9.05.2011)
Number of batches limited by MKE heating
Everything “low”:
  losses (<5 %)
  transverse emittance (< 2.5 μm?)
  but intensity also (1.15x1011 max @ 450 GeV)
Possible reasons for low transverse emittance:
  low e-cloud (no significant venting for last 2 years, scrubbing with 50 ns beam?…) → tbc
  careful transverse setting-up (ADT and chromaticities)
  smaller injected emittances ? → tbc

## Slide 4: 50 ns beam
High intensity beam (1.6 x 1011 @ 450 GeV)
  unstable on flat bottom → possible cure: larger injected longitudinal emittance + optimised gains in LLRF
  violently unstable at the end of the ramp → cure: optimised emittance blow-up in the SPS (need dedicated MD session in next MD block)
PS-SPS transfer
  with 20% larger emittance: improved stability in the SPS (still at the limit on FT without emittance blow-up in the SPS)
  no visible degradation in beam transmission (~94-96%) –more detailed analysis needed

## Slide 5: Q20 cycle
Very low emittances for very high intensities
  space charge limit?
  how losses can be taken into account?
Next steps:
  multi-binch operation
  (in)stability on flat top (blow-up is not desirable)
  voltage program for multi-bunch beam