## Slide 1: LIU-SPS 2011
Wrap-up discussion points

## Slide 2: Main results from 2011
LHC can digest half-nominal transverse emittance
SPS can deliver nominal 25 ns intensity in ~3 um, and almost ultimate 50 ns intensity in 2 um
Smaller emittances in SPS for 50 and 25 ns beams
(Where) has the ecloud gone?
Ecloud mitigation industrialisation works
Q20 optics deployment progress
Q20 instability limits progress
PS-SPS longitudinal transfer studied
Limits still there from MKE heating and ZS sparking
BI upgrades are not for overnight
Transverse emittance measurement crucial, but still shaky
High bandwidth feedback needs kick-start for implementation

## Slide 3: SPS brightness
Can we draw all the limitation curves in the intensity-emittance diagram for 25 and 50 ns?
  Single bunch
    Space charge, TMCI, injection matching, ...
  Multibunch
    RF power, coupled bunch instability, electron cloud (coherent and incoherent), ZS, MKE, ...
Do we know by how much the upgrades will move them??

## Slide 4: Smaller emittances in 2011
Are we confident this is a real change, or the BI ‘improvements’?
  LHC emittances confirm 2 – 2.5 um from SPS
  Can we check LHC emittances for 2012??
Is it coming from injectors - double-batch 50 ns beam?
Quantitatively how much better is 25 ns beam in 2011?
Can improvement be attributed to SPS scrubbing, or SPS setup? What else?

## Slide 5: Ecloud in 2011
Where has it gone?
  What SEY values are consistent with observed thresholds?
  Are these SEY values explainable from ‘operational’ 50 ns scrubbing?
    Saw this for LHC where initial 25 ns injection was much easier than 50 ns
What are the essential things to demonstrate in 2012?
  Scrubbing test period
    Effective scrubbing with lower average beam power?
    Quantification of SEY values and ecloud density
    Measurement techniques (stable phase??)
    Performance reach for 25 ns beams
  Mitigaton measure tests
    Validation of coated dipoles with in-situ monitors
    Understand vacuum pressure at coated dipoles – theoretical progress? Desorption?
    Removal of coatings, mag measurement of coated dipoles, ...
Big decision to make at end of 2012..coat or scrub.

## Slide 6: Q20 optics
Are results with single bunches as expected?
  TMCI limits, working point optimisation, exy vs. Ib, ...
  RF aspects
  Orbit control, dogleg compensation, injection, extraction, dump, matching, ...
Are results with multibunch beams as expected?
  Losses, instabilities
  Longitudinal aspects

## Slide 7: PS-SPS longitudinal transfer
What are the implications of the results?
  Any scope for improving beam loss at injection?
Studies for 2012

## Slide 8: Limits from MKE and ZS
MKE heating should cease to be a limit for 2014
  Any detailed impedance measurements planned to check differences 2011-2012?
ZS sparking problematic for ‘operatically driven’ intensity increases
  Modulation of voltage on PPM basis for ion traps only
  Negative bump at ZS not tested – plan for 2012?
  Longer term – not much prospect of major improvement
Should we plan new filling schemes for these ‘total intensity’ limits (e.g. 3 batches only?!)
What about longer bunches or more bunch shape control?

## Slide 9: BI upgrades
A lot of effort from the experts, but still need better approach for transverse profile measurements in 2012
  Sequencer driven measurements and configuration for all operational cycles?
  Systematic logging of profiles?
  Expert involvement??
Other upgrades defined but now need implementation – already late
  Attack this early in 2012
  Regular follow-up in coordination meeting (invite Benoit?)

## Slide 10: High bandwidth feedback
Need urgently to define project plan in detail and assign people to studies and design
  Identify names at CERN and in US
  Setup milestones and project workpackage responsibles
  Simulation effort?