## Slide 1: SPS flanges Simulations & Measurements Update
Fritz Caspers and Jose E. Varela

## Slide 2: Outline
Introduction
The ‘Thomas Bohl’
Simulations
Measurements
Next Steps
Conclusions

## Slide 3: Introduction
We continue to search for possible causes of the suspected 1.4GHz microwave instability in the SPS.
The ‘Thomas Bohl’ has been completed.
  We now have a list of the different flange setups, location and total number.
The three ‘most numerous’ flange setups have been simulated.
  We have now impedance and R/Q.
More refined measurements have been carried out.
  Still, one more version of the measurement set-up is under preparation (expected for mid September).

## Slide 4: Outline
Introduction
The ‘Thomas Bohl’
Simulations
Measurements
Next Steps
Conclusions

## Slide 5: The ‘Thomas Bohl’
Disclaimer: The ‘Thomas Bohl’ does not include the LSSs

## Slide 6: The ‘Thomas Bohl’
 | Flange | 1 | 2 | 3 | 4 | 5 | 6 | Total
156 | QF-MBA | 14 | 14 | 15 | 13 | 13 | 14 | 83
156 | MBA-MBA | 2 | 1 | 2 | 4 | 3 | 2 | 14
156 | QD-QD | 16 | 16 | 18 | 16 | 17 | 16 | 99
156 | QF-QF Non-enamelled | 8 | 8 | 5 | 9 | 9 | 7 | 46
156 | QD-QD Non-enamelled | 12 | 13 | 12 | 12 | 14 | 12 | 75
219 | BPV-QD | 14 | 15 | 16 | 15 | 17 | 13 | 90
219 | BPH-QF | 16/12 | 15/7 | 18/10 | 18/12 | 18/11 | 17/11 | 102/63
Analysed combinations

## Slide 7: Outline
Introduction
The ‘Thomas Bohl’
Simulations
  BPV QD-QD enamelled flange
  BPV QD-QD non-enamelled flange
  BPH MBA-MBA enamelled flange
  Total Impedance so far
Measurements
Next Steps
Conclusions

## Slide 8: Simulations
HFSS models for the enamelled QD-QD and MBA-MBA+bellow flanges.
QD-QD
MBA-MBA

## Slide 9: Simulations – QD-QD enamelled flange
Frequency [GHz] | Impedance | Q | R/Q
1.57 | 0.25kΩ | 138 | 1.8
1.89 | 5.5kΩ | 925 | 6
Modulus of the voltage for a 1W plane wave source.

## Slide 10: Simulations – QD-QD non-enamelled flange
Frequency [GHz] | Impedance | Q | R/Q
1.8 | 78kΩ | 9350 | 8.5

## Slide 11: Simulations – MBA-MBA enamelled flange
Frequency [GHz] | Impedance | Q | R/Q
1.41 | 38kΩ | 1000 | 38
Under sampled bell

## Slide 12: Simulations – MBA-MBA enamelled flange
Ez (t=0)

## Slide 13: Simulations – Total Impedance so far
Freq [GHz] | Num. of elements | Impedance | R/Q
1.41 | 97 | 3.68MΩ | 3686
1.57 | 99 | 50kΩ | 178
1.8 | 75 | 5.85MΩ | 637
1.89 | 99 | 544kΩ | 594

## Slide 14: Outline
Introduction
Simulations
MBA-MBA enamelled flange with bellow
  Previous Wire Measurement
  Shielded BPH Wire Measurement
  Reflection Measurements
Next Steps
Conclusions

## Slide 15: Measurements – Previous Meas.
Last meeting we showed a not so clear wire measurement of a BPH.

## Slide 16: Measurements – Shielded BPH
New wire measurement once the pick-up has been shielded.
Rappel: TE and TM resonant mode classification is only valid for ‘pillbox’ cavities.
Very thin wire used. ≈0.1mm

## Slide 17: Measurements – Reflection Meas.
Reflection measurement with a probe.
Weak coupling checked via Smith Chart

## Slide 18: Measurements – Reflection Meas.
Reflection measurement with a probe. Coaxial mode damping.
Ferrite + foam to damp the coaxial resonances created by the probe.

## Slide 19: Measurements – Reflection Meas.
Reflection measurement with a probe. Q measurement.
Measured
Q = 110

## Slide 20: Measurements – Transmission Meas.
Transmission measurement with two probes.
Weak coupling checked via Smith Chart

## Slide 21: Outline
Introduction
Simulations
Measurements
Next Steps
Conclusions

## Slide 22: Next Steps
Simulations
  Complete all possible flange combinations.
  Special attention to the QF-QF non-enamelled case.
  Find a way to overcome current limitations.
Measurements:
  Wait for the new set-up. Expected for mid september.
Suggestions?

## Slide 23: Outline
Introduction
Simulations
Measurements
Next Steps
Conclusions

## Slide 24: Conclusions
We have values for the impedance and R/Q of three of the most numerous flange combinations.
After shielding the pick-up, the BPH flange measurements are cleaner. A Q of 120 has been measured for the 1.4GHz resonance.
Simulations and Measurements clearly show a 1.4GHz resonance.
  Whether or not, this resonance is responsible for the instability is left for discussion.