## Slide 1: Latest results from simulations of intensity effects in the SPS
Theodoros Argyropoulos, Juan Esteban,
Elena Shaposhnikova, Helga Timko, Jose Varela
BE-RF-BR

## Slide 2: Outcome of the previous meeting
Theodoros’ code
fr = (1.35–1.45) GHz
Q = 5–10
Rs = (300–400) kΩ
R/Q < 40 kΩ
Headtail
Q has a wide range
For Q = 10—20
R/Q = (20–30) kΩ
For Q = 600
R/Q = (10–15) kΩ
About a factor 2 difference in Rs between the two codes.

## Slide 3: What’s new
Code-to-code comparison
  We performed benchmarking simulations between Theodoros’ code, Headtail, and ESME
    Within about ~10 %, we get the same spectra for de-bunching
    Headtail-simulated values are confirmed
Changes in the impedance model
  Updated impedance for BPMs and Zs
  Preliminary model of flanges thanks to Jose’s simulations

## Slide 4: SPS impedance model (1)
Cavity contributions
Kicker contributions
fr (MHz) | Rsh (MOhm) | Q | R/Q (kOhm)
200.222 | 2.86 | 150 | 19.07
200.222 | 1.84 | 120 | 15.33
629 | 0.388 | 500 | 0.78
800.888 | 1.94 | 300 | 6.47
fr (MHz) | Rsh (MOhm) | Q | R/Q (kOhm)
44 | 0.026 | 11 | 2.36
305 | 0.0025 | 12 | 0.21
570 | 0.038 | 1 | 38.00
1400 | 0.02 | 1 | 20.00
3000 | 0.018 | 1 | 18.00

## Slide 5: SPS impedance model (2)
BPM + Zs contributions (preliminary)
fr (GHz) | Rsh (MOhm) | Q | R/Q (kOhm)
0.885 | 0.0146 | 482 | 0.030
0.892 | 0.0198 | 493 | 0.040
1.052 | 0.1597 | 773 | 0.207
1.062 | 0.1903 | 773 | 0.246
1.069 | 0.0454 | 654 | 0.069
1.092 | 0.0570 | 667 | 0.085
1.185 | 0.0116 | 610 | 0.019
1.215 | 0.0012 | 624 | 0.002
1.598 | 0.0426 | 672 | 0.063
1.613 | 0.5975 | 686 | 0.871
1.859 | 0.2951 | 896 | 0.329
1.960 | 0.0721 | 1993 | 0.036
0.550 | 0.49 | 2500 | 0.196
1.050 | 0.49 | 2500 | 0.196
BPMs
Zs

## Slide 6: SPS impedance model (3)
Flanges (preliminary)
fr (GHz) | Rsh (MOhm) | Q | R/Q (kOhm)
1.28 | 1.03 | 400 | 2.496
1.41* | 1.76 | 285 | 6.167
1.41 | 0.297 | 285 | 1.040
1.41 ** | 3.91 | 1828 | 2.140
1.57 | 0.017 | 55 | 0.317
1.61 | 0.559 | 980 | 0.570
1.62 | 0.121 | 120 | 1.014
1.8 | 0.651 | 881 | 0.739
1.89 | 0.186 | 175 | 1.070
* Provisional value extrapolated from a reasonably similar simulation
** Due to damping resistors, the Q value is expected to be ~10 times smaller, why R/Q is expected to remain similar

## Slide 7: The effect of damping resistors
Without damping resistors
With damping resistors
fr (GHz) | Rsh (MOhm) | Q | R/Q (kOhm)
1.41 ** | 3.91 | 1828 | 2.140
fr (GHz) | Rsh (MOhm) | Q | R/Q (kOhm)
1.41 ** | 0.391 | 183 | 2.140
No damping increases the amplitude of the 1.4 GHz peak.

## Slide 8: The effect of BPMs and Zs
With BPMs and Zs (and with damping resistors)
Without BPMs and Zs (and with damping resistors)
BPMs & Zs impedances sit in the range 1 GHz – 2 GHz, and can potentially damp the 1.4 GHz peak significantly. A precise knowledge of BPM and Zs impedance is required.

## Slide 9: Different bunch distributions (1)
    No BPM&Zs impedance
    Damping resistors
    Simulated with five different measured distributions
    On average, we still miss some impedance

## Slide 10: Different bunch distributions (2)
    No BPM&Zs impedance
    Damping resistors, w/ R/Q increased; ~15 % higher Rsh at 1.4 GHz
    Simulated w/ different measured distributions
    Fits on average
N.B. non-linear scaling between amplitude and impedance

## Slide 11: Conclusions from de-bunching simulations
Measurements and simulations are close
  Only a narrow band of 1.4 GHz R/Q fits the observations
    Simulations using the flange impedance are close to observations
    Still lack part of the impedance; how much exactly?
To pin down exactly the source of the 1.4 GHz peak
  We still have too many uncertainties in our model
    BPM and Zs impedance
    The effect of damping resistors
    Other similar elements in the ring that have not yet been counted
  Error sources in the measured spectrum:
    Fluctuations in intensity and bunch distribution

## Slide 12: Bunch lengthening on flat top
  Can bunch lengthening at flat top be explained by microwave instability?
    And can our present impedance model explain it?
    Simulations are not trivial because we don’t know the exact conditions at arrival to flat top
  Bunches are stable at flat bottom even at 4×1011 (but Landau damping can be lost and losses can be significant)

## Slide 13: Plans
De-bunching simulations
  For more precise estimates need to eliminate uncertainties
  Benchmarking of codes increased our trust in the results
Other measurements we should exploit
  Bunch lengthening at flat top (single bunches)
  Single bunch instability thresholds at flat bottom/flat top
  Longitudinal coupled-bunch instabilities
    Simulations on all these are underway