## Slide 1: Longitudinal impedance identification
T. Argyropoulos, T. Bohl, J. E. Muller, H. Timko, E. Shaposhnikova
Thanks to H. Damerau for preparing the beam
LIU-SPS BD WG
25/04/2013

## Slide 2
Same method used in the past (Measuring the Resonance Structure of Accelerator Impedance with Single Bunches, T. Bohl, T. Linnecar, and E. Shaposhnikova, PRL, 1998)
Experimental conditions:
Long single proton bunches (εL(90%) ~ (0.23 – 0.26) eVs – τinj~ (25-30) ns)
Small momentum spread (to be unstable and de-bunch slowly)
Intensity scan from 0.5x1011 to 2.0x1011 p in Q26 and 1.3x1011 to 2.7x1011 p in Q20
SPS RF off
Method:
Acquisitions of beam profiles for a period of ~90 ms (Q26) ~40 ms (Q20) after injection
followed by a Fourier analysis  The presence of resonant impedances with high R/Q and low Q leads to line density modulation at the resonant frequencies
Video of bunch profile
1.4 GHz
Example in Q26 with Np=1.58x1011 and τinj(4σ) = 28.5 ns
Measurements

## Slide 3
Example in Q26 with Np= 1x1010
Projection
Mountain range
Mode Amplitude vs Time
Contour plot

## Slide 4
Comparison with old measurements
Np = 8x1010
?
Projection
Contour plot
T. Bohl, 2007
2012

## Slide 5
Comparison Q26 - Q20
It seems to be a longitudinal resonant impedance with high Rsh/Q and low Q that causes this instability
Q20- mode amplitude projection
Np = 1.9x1010
Similar results as in Q26
Mode amplitude ratio A1400/A200 versus Intensity

## Slide 6
Simulations
Simulations to identify the parameter space of this impedance
      Using the present SPS longitudinal impedance model
        − RF systems (200 MHz + HOM (629 MHz), 800 MHz)
        − All kickers (from C. Zannini)
        − Resonance at 1.4 GHz (varying parameters, fr, Q, Rsh )
      Initial distribution:
        Tomography in the PSESME simulations until extraction to SPS
      Simulations with 2 codes (code in Matlab and HEADTAIL not fully benchmarked)
    Parameters derived from simulations
fr (GHz) | Q | Rsh (kΩ)
1.35 – 1.45 | 5 – 10 | 300 – 400

## Slide 7
Measurements vs Simulations
Simulations
Measurements
Projection
Mode Amplitude vs Time
fr=1.42 GHz Q=10, Rsh = 400 kΩ

## Slide 8
Measurements vs Simulations
Mode amplitude ratio A1400/A200 versus Intensity
In simulations: fr=1.40 GHz Q=10, Rsh = 400 kΩ

## Slide 9
Possible impedance sources
HOM in the 200 MHz or 800 MHz RF systems
Enamel flanges at each side of each BPM in the SPS
Talk of B. Salvant, LIU-SPS BD WG 12/05/2011

## Slide 10
Vacuum (isolated) flanges
Around 440 in the ring
If for each one Rsh=75 Ω  total Rsh~33 kΩ << ~300 kΩ found from simulations
Example of a BPM – H
Example of a BPM – V

## Slide 11
Vacuum flanges
Many more vacuum flanges in the ring of similar type but not isolated
How many of them ??
Example of a straight section