## Slide 1: Update on the Reduction of the SPS Vacuum Flanges Impedance
Jose E. Varela
With input from J.A Ferreira and E. Montesinos.

## Slide 2: Outline
Introduction
  The SPS Vacuum Flanges
Impedance Reduction Alternatives
  Partial Shielding + Damping
    The Wire Array
    The Sheet Shield
  Flange Redesign
Conclusions

## Slide 3: The SPS Vacuum Flanges
The longitudinal impedance of the SPS vacuum flanges has been calculated and measured during the last year.
Initial considerations on how to reduce the impedance of these elements were presented in the last LIU-SPS BD WG meeting.
The different possibilities considered previously have been narrowed down to the two most promising ones.
Some initial discussions have been held with Jose A. Ferreira and E. Montesinos to start accounting for mechanical/vacuum restrictions and look into possible implementations.

## Slide 4: The SPS Vacuum Flanges
Reminder!
It is important to differentiate between the different flange types.

## Slide 5: The SPS Vacuum Flanges
Non-enamelled QF – QF
≈26
Enamelled QF - MBA
≈ 97
Non-Shielded, enamelled BPH - QF
≈ 39 + 62
Group I
Total > 162 + 62

## Slide 6: The SPS Vacuum Flanges
Non-enamelled QD-QD
≈75
Enamelled QD-QD
≈ 99
Enamelled BPV - QD
≈ 90
Group II
Total > 265

## Slide 7: The SPS Vacuum Flanges
Longitudinal Impedance of the SPS Vacuum Flanges – Scattered Resonance Version

## Slide 8: Outline
Introduction
  The SPS Vacuum Flanges
Impedance Reduction Alternatives
  Partial Shielding + Damping
    The Wire Array
    The Sheet Shield
  Flange Redesign
Conclusions

## Slide 9
Partial Shielding + Damping (I)
An array of longitudinal wires or a thin metallic sheet can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
This solution would not short-circuit the enamel.
Wire number & thickness can be optimized.
Covering the gap on the left plays an important role.
Conceptual
Drawings
For further impedance reduction, the remaining space can be used for damping.

## Slide 10: Outline
Introduction
  The SPS Vacuum Flanges
Impedance Reduction Alternatives
  Partial Shielding + Damping
    The Wire Array
    The Sheet Shield
  Flange Redesign
Conclusions

## Slide 11
The Wire Shield (I)
An array of longitudinal can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
The ‘Wire Shield’ (highlighted in red) structure could be spot welded in 4 + 4 points to the current flange walls.
Spot Welding Points
Possible
Implementation

## Slide 12
The Wire Shield (II)
An array of longitudinal wires can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
Comparison between the longitudinal impedance of an 11 and 27 wire shields.
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Reference* | 1.4 | 144 | 1800 | 80
11 Wire Shield | 1.2 | 3.2 | 225 | 14
27 Wire Shield | 1.2 | 3.2 | 285 | 11
The gap was filled
in both cases
Red – 11 Wires
Black – 27 Wires
* Impedance of a QF-QF closed vacuum flange without damping resistor.
Factor ≈ 5 – 8 reduction in R/Q

## Slide 13
The Wire Shield (III)
An array of longitudinal wires or a thin metallic sheet can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
Comparison between the longitudinal impedance of two 11 wire shields, with and without gap
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Reference* | 1.4 | 144 | 1800 | 80
11 Wires: Filled Gap | 1.2 | 3.2 | 225 | 14
11 Wires: Unfilled Gap | 1.2 | 10.6 | 410 | 26
Red – Filled Gap
Black – Unfilled Gap
* Impedance of a QF-QF closed vacuum flange without damping resistor.
Filling the gap reduces the R/Q factor ≈2

## Slide 14
The Wire Shield (IV)
An array of longitudinal wires can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
Bead-pull measurements of a 5 wire ‘bricolage’ shield.
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Simulation | 1.2 | 10 | 346 | 29
Measurement | 1.2 | >4 | >187 | 21
The bricolage shield left a narrower gap

## Slide 15: Outline
Introduction
  The SPS Vacuum Flanges
Impedance Reduction Alternatives
  Partial Shielding + Damping
    The Wire Array
    The Sheet Shield
  Flange Redesign
Conclusions

## Slide 16
The Sheet Shield (I)
A thin metallic sheet can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
The ‘Sheet Shield’ (highlighted in red) structure could be spot welded in 4 + 4 points to the current flange walls.
The holes for the spot welding gun could be bigger or with a different shape if needed.
Conceptual
Drawings
Spot Welding Points
Holes for the spot welding gun

## Slide 17
The Sheet Shield (II)
A thin metallic sheet can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
Comparison between the longitudinal impedance of two sheet shields, with and without gap.
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Reference* | 1.4 | 144 | 1800 | 80
Sheet Shield: Filled Gap | 1.2 | 1.5 | 245 | 6
Sheet Shield: Unfilled Gap | 1.3 | 9 | 525 | 16
* Impedance of a QF-QF closed vacuum flange without damping resistor.
Factor ≈ 5 – 12 reduction in R/Q
Filling the gap reduces the R/Q factor ≈2.5
Initial
Imperfection Assessment

## Slide 18
An array of longitudinal wires can significantly reduce the R/Q of a longitudinal resonance without restricting the bellows functionality.
Bead-pull measurements of a ‘bricolage’ sheet shield.
The Sheet Shield (III)
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Measurement | 1.4 | >0.7 | >55 | 13.3
Simulation Wake | 1.3 | 9 | 525 | 16
Simulation Eigenmode | 1.3 | 8.6 | 510 | 17
The bricolage shield left a narrower gap

## Slide 19
Any combination of sheet and wires/holes should give similar R/Q reduction.
Some of these combinations have already been simulated.
The Combos
These two examples make the shield installation easier without sacrificing too much R/Q reduction.

## Slide 20: Outline
Introduction
  The SPS Vacuum Flanges
Impedance Reduction Alternatives
  Partial Shielding + Damping
    The Wire Array
    The Sheet Shield
  Flange Redesign
Conclusions

## Slide 21
Partial Shielding + Damping (II)
I.- The goal of the partial shielding is to reduce the R/Q.
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Reference* | 1.4 | 144 | 1800 | 80
Wire Array | 1.2 | 3.2 | 285 | 11
Metallic Sheet | 1.2 | 1.5 | 245 | 6
The array of metallic wires and the thin metallic sheet are ‘equivalent’ from a longitudinal mode point of view.
A factor ≈ 8-12 reduction in the R/Q can be achieved with the proposed configuration.
Both alternatives intrinsically lower the Q some extend (factor ≈6) due to the additional losses.
II.- Once the R/Q has been reduced, additional damping can be introduced to push the impedance further down.
Using current damping resistors, the resulting Q should be lower than 100.
* Impedance of a QF-QF closed vacuum flange without damping resistor.

## Slide 22
Partial Shielding + Damping (III)
A first look at the mechanical aspects including installation difficulties:
The Wire Array:
Probably, the best way to fabricate/build it would be 3D metallic printing.
  Could cause outgassing problems – To be assessed
The other building alternatives would be, in principle, more expensive but also possible.
The cost would highly depend on the number of wires (trade-off).
Installation via spot welds.
The Thin Metallic Sheet:
In principle, a very cheap solution in terms of manufacturing ( proposed by E. Montesinos ).
  Metallic Sheet
    0.15 - 0.2mm thick Stainless Steel
    Copper sheet as in the bricolage setup ( fixed with a spot welded screw )
  Stamp
  Shield Bending
Could give rise to higher impedance if certain parts are not in good contact.
  Initial study show additional high frequency modes (>2GHz).
Installation via spot welds.
Additional studies concerning induced currents in the shields, heating, how to ensure that the shield won’t go into the aperture, installation difficulties… will be needed.

## Slide 23
Partial Shielding + Damping (IV)
Very Rough estimation of cost/time:
Number of flanges to act upon: ≈165 – 200 (only Short Straight Sections considered)
  Maybe something could be done with flanges of group II.
Cost:
  The wire array: Unknown (depends on many different things)
  The thin metallic sheet: Very cheap.
For the installation:
  A team of two people would be needed
  + Moving all the BPHs
  + Moving other stuff in the SSSs.
Time
  1 day/flange
  ≈ 15-30 weeks
  Two people 15 – 30 weeks ≈ 75 kCHF – 150 kCHF
Possible synergies with other projects to reduce cost?
The SPS tunnel will be very busy during LS2 (cavity rearrangement, etc…) could cause difficulties.

## Slide 24: Outline
Introduction
  The SPS Vacuum Flanges
Impedance Reduction Alternatives
  Partial Shielding + Damping
    The Wire Array
    The Sheet Shield
  Flange Redesign
Conclusions

## Slide 25
MBA / QF Bellows
Flanges without gap
Flange Redesign (I)
This solution minimizes the impedance and is enamel compatible.
Its cost is, on the other hand, the highest.
From the impedance point of view it is clear what to do. Mechanical restrictions/difficulties have to be consider.
Schematically, one would expect to have something like:
Conceptual
Drawings

## Slide 26
Flange Redesign (II)
This solution minimizes the impedance and is enamel compatible.
Its cost is, on the other hand, the highest.
From the impedance point of view it is clear what to do.

## Slide 27
Flange Redesign (III)
Redesign of a QF-QF closed flange.
Gap filling and QF bellows.
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Reference* | 1.4 | 144 | 1800 | 80
Wire Array | 1.2 | 3.2 | 285 | 11
Metallic Sheet | 1.2 | 1.5 | 245 | 6
Redesign | 1.5 | 0.75 | 185 | 4
Of course, impedance-wise, this is the best solution.
The modes could be further damped (not straight forward).
* Impedance of a QF-QF closed vacuum flange without damping resistor.
Tweaking the vacuum seal would reduce the impedance further

## Slide 28
Flange Redesign (IV)
Redesign of a QD-QD closed flange.
Gap filling and QD bellows redesign.
Tweaking the vacuum seal or producing smaller clamps would reduce the impedance further
f [GHz] | Z [kΩ] | Q | R/Q [Ω]
1.76 | 18.7 | 1050 | 18
2.45 | 17.2 | 1415 | 12
Current Impedance for this type of flange
New QD bellows

## Slide 29
Flange Redesign (V)
Very Rough estimation of cost/time:
Number of flanges to act upon: ≈425 – 550 (only Short Straight Sections considered)
  Considering both flange groups.
Cost:
  ≈ 4 – 6 kCHF per position.
  425 - 550 flanges ≈ 1.5 - 3 MCHF (should be lower for a big order)
For the installation:
  A team of three people would be needed
  + Removing all the BPMs (cutting and welding new flange)
    Transport issues could arise
  + Changing the pipe of Sextupoles/Octupoles.
  Cutting and welding in rad workshop ( could be arranged temporarily in the tunnel )
Time
  ≈ 15-30 weeks
    With harmonic workflow 4 day/flange
    2 days per Sextupole / Octupole
  Three people 15 – 30 weeks ≈ 110 kCHF – 225 kCHF
Possible synergies with other projects to reduce cost?
The SPS tunnel will be very busy during LS2 (cavity rearrangement, etc…) could cause difficulties.

## Slide 30: Outline
Introduction
  The SPS Vacuum Flanges
Impedance Reduction Alternatives
  Partial Shielding + Damping
    The Wire Array
    The Sheet Shield
  Flange Redesign
Conclusions

## Slide 31: Conclusions
Two main possibilities studied:
Partial shielding:
  R/Q reduction factor 8-12 could be achieved.
  Cost of shield production is unknown
    Different possible implementations.
  Only ‘half’ of the flanges (≈200) could be acted upon.
  15 - 30 weeks of work
  Order of magnitude cost: 250 kCHF
Flange Redesign:
  Minimum impedance. R/Q reduction factor 20.
  Cost per flange 4 – 6 kCHF
  All flanges could be changed (≈550).
  15 – 30 weeks of work
  Order of magnitude cost: 1.5 - 3 MCHF
  We already have elliptical bellows in the PS
  Final solution to the problem
Both options pose logistic problems as the SPS tunnel will be very busy during LS2.
Many thanks to J.A. Ferreira and E. Montesinos.