## Slide 1: 2014 scrubbing run 2: news hot from the oven
The scrubbing team, i.e. H. Bartosik, G. Iadarola, K. Li, L. Mether, A. Romano, G. Rumolo, B. Salvant, M. Schenk, T. Argyropoulos, T. Bohl,, J. Esteban Muller,
G. Kotzian, E. Shaposhnikova, M.Taborelli
Thank to: E. Carlier, H. Damerau, B. Goddard, S. Hancock, W. Höfle, V. Kain, K. Cornelis, T. Levens, H. Neupert, G. Papotti, R. SalemmeD. Valuch, C. Yin Vallgren and the SPS OP crew

## Slide 2: Scrubbing run in week 50: overview
MD3: 26.4 s, 26 GeV/c
High intensity 25 ns beam
LHC25NS: 22.8s, 450 GeV/c
Monday
  High intensity 25 ns beam (up to 1.9e11 p/b injected) on flat bottom cycle
  Lifetime quite poor
  Instability after injection of 2nd batch
  Emittance blow-up in last part of trains (starting from 2nd batch), especially horizontal
  Clear horizontal instability at end of train
  Intensity scan during the night (but problems in PSB RF)
LHCMD4: 31s, slow ramp to 450 GeV/c
days

## Slide 3: Monday: High intensity LHC beams
Up to 1.9e11 p/b injected into the SPS
Poor lifetime, instabilities at tail of batches, emittance growth

## Slide 4: Monday: from high intensity LHC beams back to nominal

## Slide 5: Scrubbing run in week 50: overview
Tuesday
  Long acceleration cycle (firs setup with 12 bunches)
  Doublet beam (up to 1.9e11 p/b injected)
  Instabilities on the slow ramp
  Losses on flat bottom and beginning of ramp, increasing significantly with the amount of beam injected
  Doublets also on cycle with standard ramp in parallel
  Intensity on flat top similar in both cases, maximum of about 1.4e11 p/doublet
  RF problems in PS during the night
MD3: 26.4 s, 26 GeV/c
LHC25NS: 22.8s, 450 GeV/c: doublet
LHCMD4: 31s, slow ramp to 450 GeV/c: doublet
days

## Slide 6: Tuesday: attempt to accelerate doublet on slow and nominal ramp

## Slide 7: Scrubbing run in week 50: overview
Wednesday
  Scrubbing with high intensity standard beam on flat bottom cycle
  8b+4e beam on LHC cycle (1.6e11 p/b injected, 1.4e11 p/b at flat top)
    Well behaved electron cloud-wise (as predicted)
    Pressure spike on ZS (impedance?)
  BCMS in good shape (1.35e11 p/b injected, 1.15e11 p/b at flat top), but still large losses at beginning of ramp
MD3: 26.4 s, 26 GeV/c
LHC25NS: 22.8s, 450 GeV/c
8b+4e
BCMS
LHCMD4: 31s, slow ramp to 450 GeV/c
days
MD3: 26.4 s, 26 GeV/c
High intensity 25 ns beam
LHC25NS: 22.8s, 450 GeV/c

## Slide 8: Scrubbing run in week 50: overview on pressure behaviour on an arc gauge (not a-C coated)

## Slide 9: Scrubbing run in week 50: overview on pressure behaviour on an arc gauge (a-C coated)

## Slide 10: Summary
High intensity LHC beam (4 batches 72b) at 26 GeV/c
  Strong electron cloud effects
    Poor lifetime, emittance blow up at the tails of the batches
    Coherent instabilities contributing to the blow up (not suppressed by transverse damper and/or high chromaticity)
Doublet beam accelerated to 450 GeV/c
  Many transverse instabilities observed on the slow ramp
  Maximum intensity at flat top 1.3e11 p/doublet both on slow and nominal LHC filling ramp
  Beam quality strongly degraded (emittance blow up)
Other LHC beam variants tested
  8b+4e well behaved in terms of electron cloud (as expected), but sparking and outgassing on ZS (impedance problem?), up to three batches accelerated to 450 GeV/c
  BCMS in good shape, less electron cloud thanks to shorter batches, up to three batches accelerated to 450 GeV/c
  For both cases, quite large losses at start of the ramp
In general, more scrubbing accumulated, but much more still needed to allow stable operation at higher bunch intensities….

## Slide 11
Thank you for your attention!