## Slide 1: SPS Longitudinal Impedance Simulations & Measurements Update
Benoit Salvant, Carlo Zannini, Thomas Bohl, Helga Timko,
Fritz Caspers, Elena Shaposhnikova and Jose E. Varela
Acknowledgements: Jose A. Ferreira (TE-VSC_IVM),
Sebastien Calvo and Antoine Boucherie (BE-RF-PM)

## Slide 2: Outline
Introduction
SPS Longitudinal Impedance Model 2013
SPS Longitudinal Impedance Model - Update
  Flanges
  Cavities
Next Steps
Conclusions

## Slide 3: Introduction
The impedance model of the SPS is evolving with time as new elements are included in the model.
The complete SPS longitudinal impedance model, as used in beam stability simulations, will be presented today.
In addition, a preliminary version of small updates to the model will be shown as ‘work in progress’.

## Slide 4: Outline
Introduction
SPS Longitudinal Impedance Model 2013
SPS Longitudinal Impedance Model- Update
  Flanges
  Cavities
Next Steps
Conclusions

## Slide 5: 2013 SPS Longitudinal Impedance Model (I)
Element | f [GHz] | a (μs) | Z [kΩ] | Q | R/Q [Ω]
200 TWS - 43 cell | 0.200 | 3.56 | 1752 | G. Dome SPS/ARF/77-11 | -
200 TWS - 54 cell | 0.200 | 4.47 | 2760 |  | -
800 TWS | 0.800 | 2.07 | 1938 |  | -
200 TWS HOM | 0.629 | - | 388 | 500 | 780
  , where .
Updated in LIU-SPS BD WG meeting 19/09/2013. Talk of H. Timko.

## Slide 6: 2013 SPS Longitudinal Impedance Model (II)
Element | Enamel | Resistor * | Num. | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Flanges [ Simulation Table ] * Damping Resistors have not been included in Simulations. This column states whether or not the flange SHOULD have a damping resistor inside (and its type). ** The damping resistors were estimated to halve the Q of enamelled flanges. Latest measurements showed a lower reduction, 1.26, on a different set-up. For non-enamelled flanges, the damping resistors are estimated to lower the Q by a factor of 10. *** Survey not completed. Waiting for final confirmation from vacuum group about these percentages. ! Damping resistor presence percentage is assumed to be identical to the *** case. !! The effect of the LONG damping resistors has not been estimated. In this table, it is assumed to be identical to a SHORT damping resistor. | Yes | No | 90 | 1.210 | 633 | 315 | 2010
 | Yes | Long | 39 | 1.280 | 499 | 200 !! | 2495
 | Yes | Short | 90% of 83 ! | 1.410 | 722 | 134 ** | 5388
 | Yes | No | 10% of 83 ! | 1.410 | 160 | 268 | 597
 | Yes | Short | 90% of 14 ! | 1.410 | 133 | 143 ** | 930
 | Yes | No | 10% of 14 ! | 1.410 | 30 | 285 | 105
 | No | Short | 90% of 26 *** | 1.410 | 449 | 242 ** | 1855
 | No | No | 10% of 26 *** | 1.410 | 377 | 1828 | 206
 | Yes | No | 99 | 1.570 | 17.4 | 55 | 316
 | No | No | 20 | 1.610 | 588 | 980 | 600
 | Yes | Long | 39 | 1.620 | 61 | 60 !! | 1016
 | No | No | 75 | 1.800 | 651 | 881 | 739
 | Yes | No | 99 | 1.890 | 187 | 175 | 1070

## Slide 7: 2013 SPS Longitudinal Impedance Model (III)
Element | Type | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
BPMs Values calculated by B. Salvant: [LIU-SPS BD WG 08/06/2013] | BPH | 0.885 | 14.6 | 482 | 30
 | BPH | 0.892 | 19.8 | 493 | 40
 | BPH | 1.052 | 159.7 | 773 | 207
 | BPH | 1.062 | 190.3 | 773 | 246
 | BPV | 1.069 | 45.4 | 654 | 69
 | BPV | 1.092 | 57 | 667 | 85
 | BPV | 1.185 | 11.6 | 610 | 19
 | BPV | 1.215 | 1.2 | 624 | 2
 | BPH | 1.598 | 42.6 | 672 | 63
 | BPH | 1.613 | 597.5 | 686 | 871
 | BPH | 1.859 | 295.1 | 896 | 329
 | BPV | 1.960 | 72.1 | 1993 | 36

## Slide 8: 2013 SPS Longitudinal Impedance Model (IV)
Blue – Flanges
Red – BPMs
Black – Flanges + BPMs
1.4GHz Flanges
1.2GHz Flanges
1.6GHz BPMs + Flanges

## Slide 9: 2013 SPS Longitudinal Impedance Model (V)
Element | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
SPS Kickers Fit (8 resonator model) Impedance calculated by C. Zannini [LIU-SPS BD WG meeting 21/03/2013] Fit by H. Timko [LIU-SPS BD WG meeting 19/09/2013] | 0.044 | 26 | 10 | 2600
 | 0.150 | 1 | 1 | 1000
 | 0.310 | 2 | 5 | 400
 | 0.346 | 1 | 10 | 100
 | 0.550 | 5 | 1 | 5000
 | 0.810 | 20.5 | 1 | 20500
 | 1.500 | 12 | 1 | 12000
 | 3.000 | 14.5 | 1 | 14500
Blue – Re(Z)
Red – Im(Z)
Black - Fit

## Slide 10: Total 2013 SPS Longitudinal Impedance Model (I)
Blue – Re(Z)
Red – Im(Z)
200MHz TWC
800MHz TWC
Flanges

## Slide 11: Total 2013 SPS Longitudinal Impedance Model (II)
200MHz TWC
800MHz TWC
Blue – Flanges
Red – BPMs
Black – Total
630MHz TWC HOM

## Slide 12: 2013 SPS Longitudinal Impedance Model Main Resonant Impedance Sources
Element | Number | f [MHz] | Z [kΩ] | Q | R/Q [Ω]
Serigraphy | 18 | 44 | 26 | 11 | 2400
200 TWC – 54 cell | 2 | 200 | 2760 | 150 | 18400
200 TWC – 43 cell | 2 | 200 | 1752 | 120 | 14600
200 TWC - HOM | 4 | 630 | 388 | 500 | 780
800 TWC | 2 | 800 | 1938 | 300 | 6460
Kickers | 18 | 810 | 20.5 | 1 | 20500
Vac. Flanges | 129 | 1200 | 630 + 500 | 250 | 4500
Vac. Flanges | 123 | 1400 | 1875 | 200 | 9300
Kickers | 18 | 1500 | 12 | 1 | 12000
Vac. Flanges | 59 | 1600 | 630 | 395 | 1600
BPM - H | 106 | 1600 | 597.5 | 686 | 871
Kickers | 18 | 3000 | 14.5 | 1 | 14500
Approximate values.
Highlighted in red biggest impedance contributors.

## Slide 13: 2013 SPS Longitudinal Impedance Model Included Im( Z )/n Contribution
Element | Number | Source | Im( Z )/n [Ω] | Fmax [MHz] | Im( Z )/n [Ω] Included in the Model
200 TWC – 54 cell | 2 |  |  |  | 
200 TWC – 43 cell | 2 |  |  |  | 
200 TWC - HOM | 4 |  |  | 200 ? | 0.055
800 TWC | 2 |  |  |  | 
Kickers | 8 |  |  |  | 
Vac. Flanges | 589 | Carlo | 0.954 | 300 – 400 ? | 0.532
BPM - H | 106 | Benoit | 0.106 | 300 – 400 ? | 0.063
BPM - V | 96 |  | 0.048 |  | 
Calculated by Carlo
Im(Z)/n included in the model:
0.65 Ω + TWC cavities + Kickers
Non-included ‘known’ contributions:
0.5 + Resistive Wall – Space Charge
± Low Freq. Enamelled Flange Resonance

## Slide 14: Outline
Introduction
SPS Longitudinal Impedance Model 2013
SPS Longitudinal Impedance Model- Update
  Flanges
  Cavities
Next Steps
Conclusions

## Slide 15: Im(Z)/n Steps - Contribution
Step Type | Enamel | Num. of Steps | First Order Approx. | Im(Z)/n slope [Ω/GHz] |  | Total Slope [Ω/GHz] |  | Total Im(Z)/n | Slope Up to [MHz]
 |  |  | !! | Simulations by Carlo |  |  |  |  | 
QD - QD | No | 82 | 277 | 10.25 | 840 |  | 0.0365 |  | 400
 | Yes* | 101 |  |  | 1035 |  | 0.0449 |  | 400
BPV – QD | Yes* | 94 |  |  | 970 |  | 0.0418 |  | 400
VVSA - QD | No | 18 | - | - | - |  | - |  | -
156 - QD | No | 19 | 19 | 20.5 | 390 |  | 0.0169 |  | 500
QF - 156 | No | 42 | 128 | 40.5 | 1701 |  | 0.0738 |  | 500
 | Yes* | 86 |  |  | 3483 |  | 0.1511 |  | 500
MBA - 156 | No | 35 | 44 | 43 | 1505 |  | 0.0653 |  | 400
 | Yes* | 9 |  |  | 387 |  | 0.0168 |  | 400
156 – QF | No | 58 | 58 | 40.5 | 2349 |  | 0.1019 |  | 500
156 - MBA | No | 114 | 114 | 43 | 4902 |  | 0.2127 |  | 400
BPH - QF | Yes* | 37 | 37 | 88 | 3256 |  | 0.1413 |  | 500
No bellow | QF-QF | 17 | 17 | 21 | 357 |  | 0.0155 |  | 400
 | MBA-QF | 4 | - | - | - |  | - |  | -
268 - 156 | No | 21 | 21 | 17 | 357 |  | 0.0155 |  | 300
MBB – 156 | No | 22 | 22 | 32 | 704 |  | 0.0305 |  | 500
Steps Included Above |  | 759 |  | First Order Approx. |  |  | 0.9645 |  | 
Total Step Count |  | 855 | Missing Steps in the Approx. = 118 (14%) |  |  |  |  |  | 
* We know that the enamelled flanges have low frequency resonances.
25MHz measured by Fritz in the tunnel (next slides).
5MHz measured on a QD-QD flange in the lab.
!! Several step types have been assumed to be identical.

## Slide 16: Im(Z)/n Steps - Fritz Measurements (I) LIU-SPS BD meeting 25-04-2013
Measurement on ENAMELLED flange BPH 31998
Imaginary Part of the reflection coefficient

## Slide 17: Im(Z)/n Steps - Fritz Measurements (II) LIU-SPS BD meeting 25-04-2013
Measurement on a NON-ENAMELLED flange LOE 32002
Imaginary Part of the reflection coefficient

## Slide 18: Im(Z)/n Steps - Fritz Measurements (and III)
v
Enamelled Flange
25MHz Resonance
Non-Enamelled Flange

## Slide 19: Outline
Introduction
SPS Longitudinal Impedance Model 2013
SPS Longitudinal Impedance Model- Update
  Flanges
  Cavities
Next Steps
Conclusions

## Slide 20: Travelling Wave Cavity Impedance Model (I)
Element | f [GHz] | a (μs) | Z [kΩ] | Q | R/Q [Ω]
200 TWS - 43 cell | 0.200 | 3.56 | 1752 | G. Dome SPS/ARF/77-11 | -
200 TWS - 54 cell | 0.200 | 4.47 | 2760 |  | -
800 TWS | 0.800 | 2.07 | 1938 |  | -
200 TWS HOM | 0.629 | - | 388 | 500 | 780
  , where .
Current TWC impedance model
Problem with this is that the group velocity is frequency dependant and not symmetric (with respect to the cavity’s center frequency).
a = Lcav/vg(w)

## Slide 21: Travelling Wave Cavity Impedance Model (and II)
G. Dome’s equations when the frequency dependent group velocity is taken into account.

## Slide 22
200MHz Cavity – Standing Wave (I)
A Bead-Pull measurement set-up has been built to characterize the SPS cavities.
Comparison between simulated and measured field profiles (Cavity in Standing Wave mode).
  Blue – Mean field profile (10 traces)
  Red – Error bars
  Black - Simulation
 | Resonant freq. [MHz] | Q | R/Q
Simulation | 199.872 | Q0 = 20770 | 508
Measurement | 198.716 | QL = 14950 ± 0.1% | 542 ± 1%
PRELIMINARY RESULTS

## Slide 23
200MHz Cavity – Standing Wave (and II)
Fundamental pass-band R over Q comparison.
Simulation results have been displaced -1MHz.
PRELIMINARY RESULTS

## Slide 24: Outline
Introduction
SPS Longitudinal Impedance Model 2013
SPS Longitudinal Impedance Model- Update
  Flanges
  Cavities
On-going efforts
Conclusions

## Slide 25
Damping Resistor Influence Assessment
All the SPS cavity-like transitions were filled with damping resistors by G. Dôme back in 1973.
Simulating the effect of the damping resistors is tricky. So far, their effect has not been simulated reliably.
First measurements show that damping resistors can reduce up to 10 times the unloaded Q of a cavity.
Additional measurements under preparation.
 | MBA-MBA Enamelled Flange * |  | Non-Enamelled Cavity ** | 
 | NO Resistor | WITH Resistor | NO Resistor | WITH Resistor
f [GHz] | 1.49 | 1.49 | 1.417 | 1.411
Q0 | 340 ± 5% | 270 ± 9% | 1930 ± 1% | 186 ± 1%
* The enamel coating makes the flanges OPEN resonators:
→ Low Q due to radiation losses
→ High scatter in measurements due to the impact of surrounding area.
** These measurements were made on a set-up that is not present in the SPS ring.

## Slide 26
Preliminary Longitudinal Impedance Simulations
Element | Resistor* | Type | Num. | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Unshielded Pumping Ports ! Measurements under preparation. * Damping Resistors have not been included in Simulations. This column states whether or not the flange SHOULD have a damping resistor inside (and its type). ** Inappropriate way of simulating the structure. Values have some error. *** Inappropriate way of simulating the structure. Values may have a VERY LARGE error. |  |  |  |  |  |  | 
 | 2*Long | MBA-QF ! | 17 | 1.397 ** | 383 | 2107 | 182
 |  |  |  | 1.560 *** | 2686 | 2801 | 958
 |  |  |  | 1.987 *** | 381 | 3718 | 102
 |  |  |  | 2.000 *** | 1972 | 3045 | 648
 |  | Other | 25 | ? |  |  | 
Element | Resistor | Type | Num. | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Vacuum Valves ! The inner dimensions of the valves are unknown. Measurements under preparation. Won’t be soon. 1, 2 Two different simulations with ‘reasonable’ inner valve dimensions. * Minimum number of elements in the SPS. ONLY Short Straight Sections layouts considered. |  |  |  |  |  |  | 
 | No | VVSA1 ! | 19 * | 1.214 | 390 | 450 | 866
 |  |  |  | 1.682 | 157 | 635 | 250
 | No | VVSA2 ! | 19 * | 1.544 | 532 | 573 | 928
 | No | VVSB | 24 * | ? |  |  | 

## Slide 27: Outline
Introduction
SPS Longitudinal Impedance Model 2013
SPS Longitudinal Impedance Model- Update
  Flanges
  Cavities
On-going efforts
Conclusions

## Slide 28: Conclusions
The current SPS longitudinal impedance model has been presented.
An accurate model of the SPS TWC impedance is being built by means of measurements and simulations.
Several other elements are also under study and measurements under preparation.