## Slide 1: MD: SPS Working Point Scan for High-Brightness Single-Bunch Beams
H. Bartosik, A. Oeftiger, F. Schmidt, M. Titze

## Slide 2: Motivation
What is the optimal working point for high brightness beams?
  present operation with Qx=20.13/Qy=20.18 is good for operational beam parameters
  current tune spread limit ~0.21
Explore tune diagram in vertical plane for Qy > 20.25
  limits?
  which resonances are involved?
What is the loss mechanism on the flat bottom?
  scaling of losses with brightness and with intensity?
  due to space charge or lattice resonance?

## Slide 3: Experimental Setup
Cycle: MD_26_L7200_Q20_2014_V1
  Q20 optics
  small chromaticity
  amplitude detuning corrected in horizontal plane (LOF -1)
  RF voltage 4.5MV at 200MHz (single harmonic)
  flat bottom cycle (3.3s)
Beam type: LHC_INDIV with high brightness
  intensity: 2.0e11 (± 10%)
  emittance:
    horizontal: 0.85 (± 10%)
    vertical: 1.1 (± 5%)
  bunch length: ~3.3ns
  space charge tune spread:
    horizontal: 0.10
    vertical: 0.19

## Slide 4: Wire Scanners at PS Extraction
“65.H”: epsn_x = 0.835
“85.V”: epsn_y = 1.104

## Slide 5: Working Points Studied So Far:

## Slide 6: For Each Working Point…
intensities and emittances measured at
  in: 200ms
  out: 3200ms

## Slide 7: For Each Working Point…
5 wire scanner measurements for each transverse plane,
Gaussian fits in light colours

## Slide 8: For Each Working Point…
horizontal emittance: dispersion significantly contributes to wire scanner measurements!
extract bunch length from mountain range
determine via equi-Hamiltonian
subtract dispersive contribution

## Slide 9: For Each Working Point…
emittance: linear fit, interpolation to 2e11

## Slide 10: Results: Overview

## Slide 11: Results: Tune Diagram
which resonance?
further studies with reduced brightness!
??
(during 3s, LHC flat-bottom 10.8s)
Slow

## Slide 12: Results: Tune Diagram
Improves with distance from horizontal integer resonance

## Slide 13: Results: Tune Diagram
Improves with distance from vertical integer resonance

## Slide 14: Results: Tune Diagram

## Slide 15: Results: Tune Diagram

## Slide 16: Summary and Next Steps
Summary:
wire scanner emittances @PS extraction and @SPS injection in good agreement
significant contribution from dispersion to horizontal profiles
tune diagram above Qy=0.25 seems to be accessible
  higher brightness reachable?
Next Steps:
vertical tune scan for Qx > 20.22
identify resonance (which creates losses) via
  beams with reduced brightness
  pencil beams
compare losses for beams with different brightness

## Slide 17
Thank you for your attention!