## Slide 1: Multi-bunch simulations
T. Argyropoulos,
Acknowledgements: A. Lasheen, J. E. Muller, E. Shaposhnikova
LIU-SPS BD WG 18/06/2015

## Slide 2: Introduction
Measurements during MDs in 2014/2015 for different number of bunches in single and double RF systems  instability threshold during cycle for various intensities
Macroparticle simulations using BLonD (only 12 bunches for now) to compare with measurements  verify the SPS longitudinal impedance model  identify the sources of instability (vacuum flanges etc.)  make estimations for the future.
Simulations in a single RF system  faster to run and less complications compared to double RF (phase between the RF systems due to beam loading compensation in 200 MHz)
Momentum and TWC200 voltage programs

## Slide 3: Example of simulations
Example: simulations in single RF with full SPS impedance model for
N = 9.8x1010 p/b and ε=0.5 eVs
Same data analysis as in the measurements but same bunch parameters (emittance, intensity) along the batch (not the case in measurements)

## Slide 4: Example of measurements
Example from MD at 08/10/2014
265 GeV/c
Normalized
Intensity

## Slide 5: Simulations with full Imp. model
Instability threshold during cycle for different emittances
Small changes in the stability threshold
At high intensities beam blows up early during the cycle

## Slide 6: Simulations vs measurements
For the case of ε = 0.5 eVs (similar bunch emittance with measurements)
Similar threshold at N~1x1011 p/b
Much lower for higher intensities

## Slide 7: Simulations vs measurements
For lower intensities only data from an MD in 2014  better agreement with sim of ε=0.35 eVs but much lower emittance!

## Slide 8: Simulations vs measurements
In reality the impedance of TWC200 is very much reduced by the FB/FFW.
No FB/FF models included in simulations for the moment.
Without TWC200 impedance, stability threshold at flat top is increased (Nthr~0.8E11) but lower threshold for higher intensities
With 20dB reduction of the TWC200 induced voltage: at flat top Nthr~1E11  still above 1.3E11 p/b threshold too low compared to measurements
No change in threshold with intensity as in measurements
Simulations for ε=0.5 eVs

## Slide 9: First conclusions
Some discrepancy between simulations and measurements of 12 bunches
Possible reasons:
  Difference in initial conditions (bunch by bunch variation in measurements in emittance and intensity)
  Effect of bunch distribution: F(H) = (1-H/H0)1.5 was used only
  Better simulation of LLRF (FB/FF, phase loop) should be included
  Impedance model is not complete (TWC HOM?)
  …
Nevertheless we can still estimate the contribution of different impedances

## Slide 10: Effect of vacuum flanges
Simulations without the vacuum flanges and for ε=0.5 eVs
Stability threshold at flat top is increased by almost factor of 2 (Nthr from 0.45E11 to 0.8E11)
Not the same during the ramp  possible different types of instabilities: LLD during cycle mw type at flat top(?)

## Slide 11: Effect of different impedances
Simulations to identify the effect of other impedance elements were also carried out (many more are needed).
TWC200 | + | - | + | + | - | - | - | - | 20dB less
TWC800 | + | + | + | + | + | + | + | - | +
Flanges | + | + | - | + | + | - | + | - | +
Kickers | + | + | + | - | + | + | - | + | +
HOM | + | + | + | + | - | + | + | + | +
ε=0.35 eVs | 3.5 | 6.0 | 6.0 | 7.5 |  | 10.0 |  | 4.0 | 6.5
ε=0.5 eVs | 5.5 | 8.0 | 7.5 | 9.0 | 8.0 | 12.0 | 12.0 | 6.5 | 10.5
ε=0.6 eVs | 6.5 |  | 8.5 |  | 9.0 |  | 12.5 |  | 12.5
Table: instability threshold (x1010 p/b) at flat top. The impedance elements that are written are always included.
The table needs to be completed (and understood) and also necessary to repeat it for a double RF system

## Slide 12: Summary
Removing the flanges reduces the instability threshold at flat top by almost a factor of 2
Not so much increase during cycle  different types of instabilities
Perhaps for a double RF system we are concerned mainly for the instability at flat top  reducing the impedance of the vacuum flanges will help! (to be confirmed in simulation)
Simulations in double RF are on-going  more delicate due to the phase error between the RF systems (FF/FB)  start from single bunch simulations (Alex)
In addition instability at flat bottom observed during the last MD in double RF system operation  needs to be understood and simulated