## Slide 1: Effect of 200 MHz TWC frequency shift on instabilities
M. Schwarz
LIU-SPS BD WG meeting, 28 March 2019
Acknowledgements:
A. Farricker, A. Lasheen, G. Papotti, J. Repond, E. Shaposhnikova, H. Timko, BLonD dev team

## Slide 2
Motivation
Previous simulations used model of 200 MHz TWC assumed resonant frequency at 200.222 MHz
But resonant frequencies of real cavities are shifted by [C. Vollinger et al.] -90kHz for 5-section cavity -127kHz for 4-section cavity
What is the impact of this frequency shift on (flat-bottom) instability?
Outline
Estimation based on coupled bunch theory
Simulations with 12 bunches
Comparison with measurements

## Slide 3
Coupled bunch instability
[E. Shaposhnikova, CERN-SL-99-040-HRF, 1999]
Fourier transform of unstable beam
Assume equally spaced bunches (full SPS with 25ns bunch spacing)
TWC impedance given by ‘Dome’ equation
For coupled bunch mode , frequencies are , ,
For multipole , , distribution function
Eigenvalue problem: ,
Growth rate of mode given by (negative implies growing mode)
Here we use μ=2.5, τ=3ns, 1e11 ppb

## Slide 4
Coupled bunch instability
Eigenvalue problem:
For narrow resonance, only two frequencies at contribute
Growth rates ,
Approximate growth rate:
[E. Shaposhnikova, CERN-SL-99-040-HRF, 1999]

## Slide 5
Growth rates, m=1
assuming ideally tuned cavity
shortest growth time for mode n~-12

## Slide 6
Growth rates, m=2
assuming ideally tuned cavity

## Slide 7
Instability growth times
Growth time of instability quickly decreases when cavity is detuned
Dipole mode (m=1) has the shortest growth time

## Slide 8
Simulation setup for BLonD
Initial bunches are obtained by simulating bunch rotation in the PS (no intensity effects) with fixed μ=2.0 (BLonD convention) and varying emittance
2 million macro-particles per bunch; 12 bunches
Include frequency shift of 200 MHz TWC (frequency shift of 0 kHz corresponds to fr of 200.222 MHz) Present case:
  -90 kHz for 5-section cavity
  -127 kHz for 4-section cavity
https://gitlab.cern.ch/longitudinal-impedance/SPS/tree/clean-up
Use full SPS impedance model
Phase loop; no feedback
V200=4.5 MV, Q20, at flat bottom

## Slide 9
Initial bunch profiles

## Slide 10
Threshold vs frequency shift

## Slide 11
Threshold vs frequency shift

## Slide 12
Frequency shift and feedback
Without frequency shift of 200 MHz TWC, ‘reduced’ impedance is symmetric around fr
This symmetry is broken when introducing a finite frequency shift

## Slide 13
Summary
Coupled bunch theory (for M=924 bunches) gives that mode (n,m)=(-12,1) is the fastest growing mode; growth time quickly decreases when resonant frequency is shifted
When including frequency shift in simulations, better agreement with measurements is achieved (but only few simulated bunch lengths)
Next steps
Take feedback into account
Simulate with LIU parameters (72 bunches, 2.6e11 ppb)
… continue with analyzing synchronous phase shift measurements
Thank you for your attention!

## Slide 14
Threshold vs frequency shift; fr=200.265MHz
Simulations ongoing

## Slide 15
200MHz TWC impedance
Present:
-90kHz for 5-section cavity
-127kHz for 4-section cavity
present